## Slide 1: Guidance for Light-Weight Implementations of the Internet Protocol Suite
Carsten Bormann, Ed.
Contributors:
Olaf Bergmann
Tero Kivinen
Carl Williams
Mitsuru Kanda

## Slide 2: Outline
Background
Drawing the landscape
Document structure
Techniques
  6LoWPAN
  CoAP
  API
  PANA

## Slide 3: Background
What we have
  Protocol specs: 6LoWPAN, 6LoWPAN_ND, RPL, CoAP…
What are in need
  Techniques to implement these optimized protocols
  Guidance to make the implementation small and interoperable
Objectives :
  Collect experiences from implementers of IP stacks on constrained devices
  Knowledge of the art of the literature, helpful for future practice
  Conformance with the relevant specs
  Not software engineering best practices

## Slide 5: Classes of “Constrained” Devices
Distinguish 2 rough classes of constrained nodes:
In each case, make clear which class is being targeted
(These are a starting point for making sure we discuss from the same requirements, not exact classes.)
 | Data Size | Code Size
Class 1 | ~10 KB | ~ 100 KB
Class 2 | ~50 KB | ~ 250 KB

## Slide 6: Implementation styles
Single-threaded/giant mainloop
Event-driven vs. threaded/blocking
Single/multiple processing elements
  E.g., separate radio/network processor
In mind:
  Some techniques may be applicable only to some of these styles!

## Slide 7: Roles of nodes
Constrained nodes
  Sleepy nodes
Nodes talking to constrained nodes
  To sleepy nodes
  Normally always alive
Gateways/Proxies
  To sleepy nodes
  Could be always alive
Notes: <number>

## Slide 8: Document Overview
Data Plane
  6LoWPAN
  CoAP
Control Plane
  RPL
Security
  PANA

## Slide 9: 6LoWPAN Route-Over Fragment Forwarding
Contributor: Carsten Bormann Universität Bremen TZI
cabo@tzi.org
Notes: <number>

## Slide 10: 6LoWPAN Implementation Tricks: Fragment Forwarding Technique
6LoWPAN: adaptation layer fragmentation can be needed
Route-Over happens above adaptation layer
Would have to reassemble at each hop
Better:
  Build cache entry on initial fragment
  Forward initial fragment immediately
  Forward each non-initial fragment based on cached IP header info

## Slide 11: Constrained Application Protocol (CoAP)
Contributor : Olaf Bergmann Universität Bremen TZI
bergmann@tzi.org
Notes: <number>

## Slide 12: Trivia
Why CoAP matters:
  M2M communication in constrained networks
  connect smart objects to the Internet
  Goal: HTTP equivalent for WSNs (REST)
Focus
  Class 1 devices: ~10 KiB RAM, ~100 KiB Flash
  Server applications
  Robustness/latency vs. resources (power, dynamic memory needs, static code size)
  Keep mandatory (to recognize) protocol features
Notes: <number>

## Slide 13: Message Layer Processing
Avoid fragmentation, retransmission
  minimize state maintenance and power usage (especially server side)
Must have send buffer and tick counter (or RTC)
To generate separate responses, servers must keep client's transport address and Token
Sleepy nodes
  fix up clock if interrupts are disabled during sleep
  No sleep for the first 1 or 2 retransmission cycles
Notes: <number>

## Slide 14: Message Parsing
The usual parsing strategies
Propose bit-vector for type-decoding
Some options are allowed more than once (Uri-Path):
  Could make last segment unique or collect while you parse
Notes: <number>

## Slide 15: CoAP Token Handling
CoAP: Tokens used for request-response matching in non-piggybacked responses
Needs space in packet and node
Better:
  Use default value of 0 while not pipelining
  Use non-zero values (or separate port numbers) with multiple outstanding requests

## Slide 16: (How to) Proceed From Here?
Feedback from mailing list
  Clarify which roles are talked about
  Analyze implementation cost for server and client
  Hard-coded parameters (e.g. max. payload size?)
  What about gateways and proxies?
Security implementation?
  Proposal: should be covered in the general security section
Other documents
  draft-arkko-core-sleepy-sensors
Is this the right information to put in this document?
Notes: <number>

## Slide 17: General considerations about Application Programming Interfaces (APIs)
Author: Carl Williams

## Slide 18: API
One of the roles of the API can be exactly to hide the detail of the transport protocol
uIP application interface
  Event driven API model
  Standard multi-threaded model not used
TinyOS
  Non-blocking API
    When application interface sends a message the routine would return immediately (before msg is sent)
    Call-back facility notifies app when sending is done.
    Benefit: no code runs for long periods of time; otherwise, pkt is dropped.

## Slide 19: Work in Progress
Gathering implementation experiences from IPSO developers
  Attendance of IPSO late March
  Work with API implementers in IPSO alliance

## Slide 20: Guidance for Lightweight Security Protocol
Author: Mitsuru Kanda
Presenter: Yoshihiro Ohba

## Slide 21: Minimal PANA Implementation
Protocol for Carrying Authentication for Network Access defined between PaC (PANA Client) and PAA (PANA Authentication Agent)
PaC may be sleeping
  Use PaC-initiated session
    Sleeping device can’t process an unsolicited PAA-initiated session message
  PANA ‘Ping’
    Do not use PANA ‘Ping’ for mutual liveness check
  Use PaC Initiated re-authentication
    Sleeping device can’t process an unsolicited PAA-initiated re-authentication message
PANA message optimization (reduce number of messages)
  Use Piggybacking EAP technique
  Don’t send a PTR message for PANA session lifetime expiration

## Slide 22: Next step
Integrate more organized text on security and other parts
Circulate a Questionnaire for implementers to collect information