## Slide 1: Multicast filtering practices
draft-chown-mboned-multicast-filtering-01
IETF81, Quebec
Tim Chown, tjc@ecs.soton.ac.uk
July 27th, 2011

## Slide 2: Rationale
At IETF80, raised the issue about 234.0.0.0/8 (RFC 6034) being filtered
  Where does filtering policy/guidance come from?
Agreed to get some operational feedback and summarise to a draft
  And here we are…
Also surveyed service discovery mechanisms
  The only answer given was SAP

## Slide 3: Responses
Asked academic-oriented lists
  janet-multicast@jiscmail.ac.uk
  wg-multicast@intrnet2.edu
Got about a dozen responses
  For border and MSDP peer filters
Some referred to texts
  Internet2 Multicast Cookbook
  IPv4 Multicast on JANET
The draft currently aggregates responses

## Slide 4: Scopes for filtering
Organisation border
MSDP peer
  Likely to be similar to border, except for SSM
Intra-organisation
  e.g. multi-site
Subnet
  Handling ‘broken’ implementations
    e.g. of uPNP for a certain printer

## Slide 5: Topics raised (1)
How strict to be
  No respondents mentioned 234.0.0.0/8.
TTL-based filtering seems obsolete
Some commonalities in filtering of specific IANA-assigned addresses under 224.0.0.0/8
  How arbitrary is the filter list here?
  One responder gave hit counts on filters
Varying use of RFC 2365 scoping within sites

## Slide 6: Aggregate filter list
224.0.1.1 NTP
224.0.1.2 SGI-Dogfight
224.0.1.3 Rwhod
224.0.1.8 SUN NIS+
224.0.1.20 any private experiment
224.0.1.22 SVRLOC
224.0.1.24 microsoft-ds
224.0.1.25 nbc-pro
224.0.1.35 SVRLOC-DA
224.0.1.38 Retrospect
224.0.1.39 cisco-rp-announce
224.0.1.40 cisco-rp-discovery
224.0.1.41 gatekeeper
224.0.1.60 hp-device-disc
224.0.1.65 iapp
224.0.1.76 IAPP lucaent-avaya-ap
224.0.2.1 rwho
224.0.2.2 SUN RPC
224.0.2.3 EPSON-disc-set
224.0.23.1 Ricoh-device-ctrl
224.0.23.2 Ricoh-device-ctrl
224.1.0.1 Cisco Aironet
224.1.0.38 Retrospect
224.2.0.2 Altiris Rapideploy
224.2.0.3 Altiris Rapideploy
224.77.0.0/16 Norton Ghost
224.101.101.101 Sun Sunray
225.1.2.3 Altiris Server/Agent
226.77.0.0/16 Norton Ghost
229.55.150.208 Norton Ghost
231.0.0.0/8 ?
234.21.81.1 Limewire
234.42.42.0/30 ImageCast
234.42.42.32/31 ImageCast
234.42.42.40/30 ImageCast
234.142.142.42/31 ImageCast
234.142.142.44/30 ImageCast
234.142.142.48/28 ImageCast
234.142.142.64/26 ImageCast
234.142.142.128/29 ImageCast
234.142.142.136/30 ImageCast
234.142.142.140/31 ImageCast
234.142.142.142 ImageCast
239.0.0.0/8 Scoped groups
239.252.0.0/14 Scoped groups
239.234.5.6 ECopy ShareScan

## Slide 7: Topics raised (2)
Filter multicast sourced from IPv4 private address range, or from 169.254.0.0/16, 192.0.2.0/24 or 127.0.0.0/8
Some use of rate limiting, esp. for SAP or MSDP SA bursts
Filtering BSR packets at border
Multicast often routed around unicast firewall
Multicast on wireless infrastructure
Very little mention of IPv6 in responses
  Might include Router Advertisements

## Slide 8: Next steps?
Is this text useful?
  If so, a living document or work towards RFC?
  Danger of practices changing, new allocations (e.g. like 234.0.0.0/8), etc
Quite drafty at present, so structure needs tidying up
  Probably arrange by scopes and issues
Need more IPv6 considerations added
Co-author(s) welcomed