## Slide 1: Multicast Extensions to DS-Lite Technique in Broadband Deployments draft-qin-softwire-dslite-multicast-04
Xiaohong Deng

## Slide 2: Context
  Deliver multicast service from IPv4 source to IPv4 reciever over IPv6 network by encapsulation

## Slide 3
IPv4 Source
IPv4 Receiver
mAFTR
mB4
IGMP
MLD
QR
MLD Querier
IPv6 PIM
IPv4 PIM
IPv4 Flows
IPv4-in-IPv6 Flows
Stateless IPv4-IPv6 PIM Interworking Function
Stateless IGMP-MLD Interworking Function
Stateless encapsulation
&
IPv4 -> IPv6 header mapping
of multicast flows
Overall procedures with involved interworking functions:
Need to provision the mB4 with mPREFIX64 and uPREFIX64
IPv4 Realm
IPv6 Realm
IPv4 Flows
DR
R
S
IPv4 Realm
Stateless de-encapsulation of multicast flows
CPE

## Slide 4: Addressing
Address Building
  Use [I-D.boucadair-behave-64-multicast-address-format] to build multicast IPv4-embedded IPv6 addresses
  Use [RFC6052] to build unicast IPv4-embedded IPv6 addresses representing IPv4 sources in the IPv6 realm
All address translation in interworking functions are stateless

## Slide 5: Operation Consideration
The data packets received by the reciever are identical to the packets sent by the source regardless the mechanism
RP Locatition for ASM
Preserve lay 2 operations (IGMP snooping/proxy)
Location of mAFTR

## Slide 6
IPv4 Source
IPv4 Receiver
mAFTR
mB4
IGMP
MLD
QR
MLD Querier
IPv6 PIM
IPv4 PIM
Stateless IPv4-IPv6 PIM Interworking Function
Stateless IGMP-MLD Interworking Function
DR
R
S
CPE
Location of mAFTR
QR
MLD
IGMP
IPv4 PIM
MLD Querier

## Slide 7: Comments & Questions
Questions?
Anybody interested to participate?
  Join the discussion in softwires WG/Mailing list