## Slide 1: Applications Test Results in MIF environment draft-zheng-mif-apps-test-02.txt
IETF 81 Quebec City

## Slide 2: Introduction
Applications
  Windows 7: ping, IE 9, Live Messenger 2009, Skype 5.1, Firefox 3.6, Google Earth 6
  Fedora 13: ping and ping6, Skype 2.2, Firefox 3.6, Google Earth 6
Scenarios
  Host has one network adapter with dual stack
  Host has two network adapters respectively with IPv6 and IPv4
Transition solutions
  AplusP [I-D.ymbk-aplusp]
  DS-Lite [I-D.ietf-softwire-dual-stack-lite]
  NAT64[RFC6145]/DNS64 [RFC 6147]
  the combinations of them

## Slide 3: Scenario 1: One network adapter with dual stack
Test results on Windows
  Ping, IE and Firefox: IPv6 has high priority if AAAA resource record is available;
  Google Earth: IPv6;
  Skype and Live Messenger: IPv4 (because AAAA resource record is unavailable)

## Slide 4: Scenario 1: One network adapter with dual stack
Problems and suggestions on Windows 7
  Windows 7 always first queries a host name's A record, and if it receives an NXDOMAIN it will not query for an AAAA record.
  Windows 7 should ask for both type records in each DNS lookup or a host name that has only an AAAA record should have a CNAME which points to the AAAA.
Test results on Fedora
  The addresses of DNS Servers are configured in /etc/resolv.conf. The configured order decides which DNS Server has high priority. Analysis of how Fedora orders its DNS servers when it is DHCP-configured is for future study.

## Slide 5: Scenario 1: One network adapter with dual stack
  IPv6 DNS Server has high priority
    Ping, Skype: IPv4 (just sending A query);
    Ping6, Google Earth: IPv6 (just sending AAAA query);
    Firefox: IPv6 has high priority if AAAA resource record available;
  IPv4 DNS Server has high priority
    Ping, Google Earth, Skype: IPv4 (just sending A query);
    Ping6: IPv6
    Firefox: IPv4, IPv6 only in the case: the AAAA record of the queried host name can be returned in the additional records section in the A query response
Problems and suggestions on Fedora
  The IPv6 DNS Server should be configured with high priority or the AAAA record of the queried host name can be returned in the additional records section in the A query response if IPv6 is wished for.

## Slide 6: Scenario 2: Two network adapters respectively with IPv6 and IPv4 connections
Test results on Windows
  The order of two adapters in which they can be accessed can be configured in Windows system. However, in our test, the order of adapters had no impact on the priority of DNS Servers.
  Case 1: The two interfaces of IPv6 and IPv4 all with IPv6 and IPv4 dual protocol stacks
    the results are same as in scenario 1

## Slide 7: Scenario 2: Two network adapters respectively with IPv6 and IPv4 connections
  Case 2: IPv6 interface with IPv6-only protocol stack and IPv4 interface with IPv4-only protocol stack
    Ping, IE and Firefox: IPv4 (most of websites), IPv6 only when the AAAA record of the queried host name can be returned in the additional records section in the A query response, such as www.kame.net;
    Google Earth: IPv4 (because only A record is got from IPv4 DNS Server);
    Skype and Live Messenger: IPv4 (because AAAA resource record is unavailable)
Problems and suggestions on Windows
  If IPv6 is wished for, the configuration of case 2 should be avoided.
Test results on Fedora
  same as in scenario 1

## Slide 8: Transition solutions in MIF
Case 1: AplusP and IPv6 provisioned Host
Case 2: DS-Lite and IPv6 provisioned Host
Test results and suggestions
  same as in scenario 1

## Slide 9: Transition solutions in MIF
Case 3: NAT64 and DS-Lite provisioned Host
  Consider a host which contains both wifi and wireless interfaces.
  When it connects a dual-stack network provided by a B4 element via wifi and also connects to an IPv6-only network via 3G/4G provided by a wireless ISP. The wireless IPv6-only networks has NAT64/DNS64 deployed.

## Slide 10: Transition solutions in MIF
  NAT64 impacts on applications and suggestions
    Live Messenger uses IPv6 to login to the server, but the IPv6 client did not send the same application layer message as the IPv4 client, so the IPv6 client (behind NAT64) failed to get reply from IPv4 server. Therefore, the application layer of Live Messenger should be IP version independent.
    There is a need for P2P applications behind NAT64 to learn the NAT64's prefix, so that IPv6 peer can talk with IPv4 peers via NAT64. Otherwise, IPv4 connectivity is required to support remaining access to IPv4 peer

## Slide 11: Transition solutions in MIF
  Test in a both NAT64 and DS-Lite accessible network and suggestions

## Slide 12: Transition solutions in MIF
    Except BitComet, which although issues both A and AAAA quires, ignores AAAA RR and only uses IPv4 to initiate communication, all the other applications first try A RR to initiate IPv6 communications, and if it fails A RR is used to initiate IPv4 communications.
    Live messenger first fails IPv6 due to DNS64 translation, so it is suggested to avoid that translation when the application uses DNS64, as described in [I-D.wing-behave-dns64-config]. Yet, after failing IPv6 Live messenger automatically switches to IPv4 by which all the rest of communication were done.
    The application layer should be IP version agnostic in order to decrease impacts introduced by IPv6 transition solutions.

## Slide 13: Thanks!