## Slide 1: Current status 3D drafts
Bert Greevenbosch
bert.greevenbosch@huawei.com
Notes: <number>

## Slide 2: Overview
Two 3D drafts:
  draft-greevenbosch-mmusic-parallax-attribute-v01
  draft-greevenbosch-mmusic-signal-3d-format-v01
Both drafts extend SDP to signal stereoscopic 3D streaming.
The first one is for static positioning of 2D objects, such as text.
The second is for signaling the format of the stereoscopic 3D video stream.
<number>

## Slide 3: Changes in draft-greevenbosch-mmusic-parallax-attribute-v01
The unit of the ParallaxInfo attribute value has been normalised to "pixels on a screen with a width of 11520 pixels".
This allows adjusting the parallax for various screen sizes, often by dividing through an integer number.
<number>

## Slide 4: Changes in draft-greevenbosch-mmusic-signal-3d-format-v01
Added two sections for the SDP offer/answer model.
Section 7 considers behaviour for the compliant device.
Section 8 considers backward compatibility with a legacy device.
  Generally, the system will fall back to 2D streaming.
  This sometimes requires re-negotiation.
<number>

## Slide 5: Compliant answerer
MUST NOT omit "3dFormat" attribute for accepted streams.
  This caters for identification of legacy answerers.
MUST NOT change value of "3dFormat" attribute.
  Ensures only offered formats can be accepted.
MAY elect to receive 2D only, by selecting one of L/R views or only the 2D stream (rejecting auxiliary stream).
SHOULD select only one 3D format, but if it selects multiple MUST be capable to receive all.
<number>

## Slide 6: Non-compliant answerer
It is anticipated that a non-compliant answerer will omit the "3dFormat" attribute.
This is used by the offerer to deduct that the answerer is a legacy answer.
The offerer is given much freedom for its response, hence the optional nature of section 8.
In general, when the answer "makes sense", the streaming MAY proceed as agreed.
Otherwise, an updated the offer MAY be required.
<number>

## Slide 7: Response to legacy answerer in case of frame packing
If the frame packing stream is selected by a legacy answerer, the offerer MAY update the offer offering only a 2D stream.
Alternatively, it MAY stream the frame packed video as it is, anticipating that the legacy answerer has other means to process the frame packed 3D video.
  Might be user input.
<number>

## Slide 8: Response to legacy answerer in case of 2D + aux, single stream
If the offerer MAY update the offer by offering only a 2D stream.
<number>

## Slide 9: Response to legacy answerer in case of 2D + aux, separate streams
If the answerer selected only the 2D stream, streaming can proceed as agreed.
If the answerer selected only the auxiliary stream, the offerer SHOULD update its offer.
If the answerer selected both streams, the server MAY update its offer.
<number>

## Slide 10: Response to legacy answerer in case of simulcast of L- and R-view
If the answerer selected only one of the streams, the offerer MAY initiate streaming as agreed.
If the answerer selected both streams, the offerer MAY update its offer, offering only one stream.
<number>

## Slide 11: Links
https://datatracker.ietf.org/doc/draft-greevenbosch-mmusic-parallax-attribute/
https://datatracker.ietf.org/doc/draft-greevenbosch-mmusic-signal-3d-format/
<number>

## Slide 12: Next step
Move both drafts to WG draft status?
<number>

## Slide 13
Thank
you!
Questions?
Thank
you!
Questions?
<number>