## Slide 1: SDP Bandwidth Attribute
draft-westerlund-avtcore-multistream-and-simulcast-00
Magnus Westerlund and Bo Burman
Ericsson

## Slide 2: IPR Disclosure
Telefonaktiebolaget LM Ericsson (publ)'s has made a Statement about IPR related to this draft in https://datatracker.ietf.org/ipr/1592/

## Slide 3: Outline
Issues with current SDP bandwidth modifiers
  Asymmetric paths and applications
  Per Payload Type Negotiation
  Multiple Streams
  Media Stream Burstiness
Solution Proposal
Way Forward

## Slide 4: Asymmetric Paths and Applications
Significantly different bandwidth between directions
  Asymmetric network restrictions (e.g. ADSL)
  Asymmetric application capabilities
End- point
End- point
VGA
HD

## Slide 5: Per Payload type Negotiation
Significantly different bandwidth between payload types
Negotiate bandwidth per payload type and direction
End- point
Alternate codecs
pt=8
pt=96

## Slide 6: Multiple Streams
Different bandwidth depending on number of streams

## Slide 7: Allowed Burstiness
Networks may contain bandwidth Filtering or Policing
Especially when QoS is used
  IMS Policy Control
  RSVP
To keep end-point within policy, the end-point needs to know more than just bandwidth
End- point
End- point
Middle Node
Middle Node

## Slide 8: Summary of Issues
Shortcommings of current SDP:
  Stating both capabilities and actual limitations when BW is asymmetric
  Negotiating bandwidth per payload type and direction
  Negotiate bandwidth on per stream basis in multi-stream sessions
  Negotiate bandwidth on aggregate level in multi-stream sessions
  Ensure that end-point know how bursty the can be.

## Slide 9: New SDP Bandwidth Attribute
b= line not possible to extend with sufficient new semantics
An attribute with modularity
  Direction: Send, Recv or Both
  Scope: Extensible and proposes support for Payload Type specific
  Semantics that specifies both interpretation and format of values
  Per source and payload type token buckets
    a=bw:recv pt=96 SMT:tb=64000:320
    a=bw:recv pt=97 SMT:tb=12200:128
  Entire media level aggregate as token bucket
    a=bw:send pt=* AMT:tb=384000:4096
  Allow for future needed semantics to be defined

## Slide 10: Way Forward
Interest in this WG to rework SDP bandwidth?
Currently part of a big draft.
  Will be split out into a MMUSIC individual draft
Additional issues / use cases that should be tackled?