## Slide 1: draft-polk-mmusic-traffic-class-for-sdp-02
29 July 11
James Polk
Subha Dhesikan

## Slide 2: What this Draft is About
Traffic Classification attribute of sessions for
  DSCP marking (individual or in groups)
  BW pool allocations (per traffic type or per mark)
  Network resource allocations
  Monitoring specific types of traffic across network
  Etc
Started with labels created by RFC 4594
  But are now proposing new labels and meanings
  i.e., not just RTP, but which type of video?
RSVP App-ID Object defined in RFC 2872
  TSVWG ID defines profiles
    WG hummed 100% for this, but not yet an official WG item

## Slide 3: What’s changed in -02
Changed framework of traffic label, now:
  Grouped (human readable) category (based on characteristics) with application type
  Allow for optional application ‘adjectives’ to further describe traffic type
  Kept the flag for whether traffic is CAC admitted or not
  Parts not understood are ignored
a=trafficclass Category.application.adjective(s)._foo._bar.admitted
delimiter
Proprietary delimiter

## Slide 4: New Attribute Format/Framework
Category component now breaks from RFC 4594
  No more
    “telephony” for audio, and “multimedia-conferencing” for video
  “Conversational” does most interactive AV
  “Multimedia-streaming” can be buffered (a lot)
  “Broadcast” (no longer “Broadcast-video”) is not buffered much
Application component defines (hey) the application
Optional Adjective components further differentiate individual applications
Standard and proprietary delimiters remain
a=trafficclass Category.application.adjective(s)._foo._bar.admitted
delimiter
Proprietary delimiter

## Slide 5: Individual Component Parts
Categories
Conversational
Multimedia Conferencing
Real-Time Interactive
Multimedia Streaming
Broadcast
Applications
Audio
Video
Text
application-sharing
Presentation-data
Whiteboarding
Web (conference) chat/instant messaging
Gaming
Virtual-desktop (interactive)
Remote-desktop
Telemetry (e.g., NORAD missile control)
Adjectives
Immersive
Desktop
Realtime-Text
web
Multiplex (i.e., combined streams)
(something to cover theater quality Netflix movies)
(something to cover YouTube)
Webcast
IPTV
Live-events (though not the buffered ones)
surveillance

## Slide 6: Known Open Issues
Biggest issue: label now defined, but do folks agree with them
  Want help to reach consensus within RAI/MMUSIC
Transport Area doesn’t like specific guidance of series of strings put together defining a single DSCP for everyone to use (i.e., “a service”)
Some in RAI think the opposite (is anyone surprised?)
  i.e., provide a default that can be overridden within any domain
Others…?

## Slide 7: What’s next?
Depends on how this has been received
  i.e., am I bleeding too much right now?
That said, Transport Area (TSVWG) plans to continue work
  It would be nice to synchronize the two areas on the topic