## Slide 1: SCTP in SDP draft-ietf-mmusic-sctp-sdp-00
Quebec City, Canada
Friday, July 29, 2011
Salvatore Loreto

## Slide 2: Multihoming
During the lifetime of an SCTP association, the
endpoints can add and remove new addresses
from the association at any point [RFC5061].
If an endpoint removes the IP address listed in its
'c' line from the SCTP association, the endpoint
MUST update the 'c' line (e.g., by sending a re-
INVITE with a new offer) so that it contains an IP
address that is valid within the SCTP association.

## Slide 3: NAT considerations
  Current NATs do not typically support SCTP. (Possible alternative: I-D.ietf-tsv-sctp-udp-encaps)
  The work on NAT traversal for SCTP is still in progress
  No extension has been defined to integrate ICE with SCTP and its multihoming capabilities either.
Therefore, the draft does not define how to describe
SCTP-over-UDP streams in SDP or how to establish and
maintain SCTP associations using ICE.