## Slide 1: Mobility Support by the Common API for Transparent Hybrid Multicast draft-irtf-samrg-common-api-03 Project http://hamcast.realmv6.org
Matthias Wählisch, Thomas C. Schmidt, Stig Venaas
{waehlisch, t.schmidt}@ieee.org, stig@cisco.com

## Slide 2: Problem: Group Communication
There are many forms of group communication:
ASM, SSM, (restricted) Broadcast, Multi-destination Routing (XCast), Content-centric Pull …
Two basic services:
  Scalable packet distribution to a receiver group
  Publish/Subscribe option with rendezvous process
Universal, easy access requires an abstract notion

## Slide 3: Problem: Multicast Technologies
There are many multicast technologies
  on different layers
  on the same layer
Programmers decide on its use
  not even DNS helps
Mobility bound to technology
Problem: Identify same group in different technologies

## Slide 4: Objectives
Provide a solution for group apps to be compiled once and run everywhere
  Make use of multicast technologies if available
  Allow for hybrid / pluralistic network conditions
  Provide a universal service access
  Decouple application success from infrastructure deployment
  Support “vertical” mobility across service instantiations

## Slide 5: Naming and Addressing
"Multicast addresses are a set of distributed application names"
        John Day (Patterns in Network Architecture)
Just use any application name?
Problem of mapping to network addresses: out of control without namespace support
Domains may run same technology but remain isolated
Domains may run distinct technologies but host members of the same group
High-level meta data type easy for programmers
Proposal: Use abstract, namespace-aware data type - URIs for late binding + new API

## Slide 6: Proposed URI Scheme
scheme "://" group "@" instantiation ":" port "/" sec-credentials
  scheme: specification of assigned ID
  group: identifies the group
  instantiation: ID of the entity that generates the instance of the group (SSM source, RP, overlay node)
  port: ID of a specific application at a group instance
  sec-credentials: optional authentication
Examples:
  ip://224.10.20.30@1.2.3.4:5000/groupkey
  opaque://mygroup.org

## Slide 7: Common Multicast API Draft
Idea: Move complexity from application to the system level
The current draft provides …
a common multicast API on app. layer that abstracts group communication from distribution technologies
abstract naming and addressing by multicast URIs
canonical mapping between naming and addressing
definition of protocol interaction to bridge multicast data between overlay and underlay

## Slide 8: Example: SIP conferencing (SSM)
INVITE sips:lucy@peanuts.com SIP/2.0
…
Contact: maddr=sip://hypnotic-talks@psychic.org
Application:
ms=createMSocket()
ms.join(URI(“sip://hypnotic-talks@psychic.org”))
Aside:
allows extension for aggregation: *-talks@psychic.org

## Slide 9: Common Multicast API & Middleware
Mapping of names to technologies at run-time
Late binding by ID Locator Split

## Slide 10: Implementation: The HAMcast stack
Application library:
    Maps API calls & ‘signaling’ to OS layer
    Easily integrates new programming languages (C++, Java)
OS Middleware:
  Separates generic multicast logic from technology-specific instantiations
  User-space process, runs once per host (C++ )
Service Modules
  Specific to multicast technologies, currently IPv4, IPv6, and Scribe-ALM

## Slide 11: HAMcast Stack Overview

## Slide 12: Mobility
Application transparent due to ID-locator split
Mobility management
  within service module (horizontal handover)
  at generic middleware (vertical + horizontal handovers)
Middleware mobility
  Holds abstract group logic (pub/sub states)
  Can dynamically add/remove technology modules
  Mobility is merely a task of the service selection
  Generic approach: Find & improve group connectivity

## Slide 13: Thank you …
More about this in the meeting of SAMRG
Today 17:40 – 19:40
Project Website:
http://hamcast.realmv6.org
Prototype for Download:
    Now version 0.3 (mobility yet to come) Check for updates