## Slide 1: Mobile IP in 4G networks
Charles Perkins
charliep@computer.org
IETF 81: July 27, 2011

## Slide 2: Problem statement
Mobile IP is specified in 3GPP protocols, but is not being used very effectively
PMIP was specified for network-controlled mobility management, but is being displaced by GTP
Authentication of user devices does not typically rely on Mobile IP
FMIP was not considered as part of any 3GPP handover solution
3GPP perhaps views IETF as “too slow”

## Slide 3: Possible elements of solution
Overall goal: enable easier evolution to IETF solutions
Enable GTP tunneling from HA
  Hardware/microcode already optimized for GTP
  Operators are already familiar with it
  GTP enables some finer-grained session control
Enable HA to use EAP-AKA’
SFF-based handovers for heterogeneous networks
  Home agent can help, based on existing MSA with UE

## Slide 4: WLAN as a “trusted network”
LTE requires high hurdles for “untrusted” networks
  Typically requires multiple authentications (e.g, via ePDG)
  Hard (impossible?) to design seamless handovers
Trusted networks can support optimized handovers
  How does WLAN present itself as a trusted network?
  One answer: by AAA-based authentication (e.g., 802.1x)
  Proposal: EAP method using HA instead of AAA

## Slide 5: Proposed clarification to the intended role of HA
Authentication intimately bound up with mobility management
IETF received no report of compromise for authentication data procedure (AFAIK)
HA can readily send/receive encrypted data (reverse tunneled) from UE
HA behind VPN gateway is poor design, performance loss
S2c available for LTE, but doesn't seem to be getting deployment