## Slide 1
81st IETF, Quebec City
draft-bernardos-mext-dmm-pmip-01
A PMIPv6-based solution for Distributed Mobility Management draft-bernardos-mext-dmm-pmip-01
Carlos J. Bernardos – Universidad Carlos III de Madrid
Antonio de la Oliva – Universidad Carlos III de Madrid
Fabio Giust – Institute IMDEA Networks & Universidad Carlos III de Madrid
Telemaco Melia – Alcatel-Lucent Bell Labs
Quebec City, MOBOPTS WG, 2011-07-28
MOBOPTS WG, 2011-07-28

## Slide 2: Motivation
Current IP mobility approaches rely on a central anchor point (either HA or LMA)
Issues:
  Sub-optimal routing
  Reliability
  Scalability
  Lack of granularity (mobility is offered on a per-mobile basis)
  Signaling overhead

## Slide 3: DMM solution overview

## Slide 4: Extending existing protocols…
Client Mobile IP (host) based
  Fabio Giust, Antonio de la Oliva, Carlos J. Bernardos, “Flat Access and Mobility Architecture: an IPv6 Distributed Client Mobility Management Solution”, 3rd IEEE International Workshop on Mobility Management in the Networks of the Future World (Mobiworld 2011)
  draft-bernardos-mext-dmm-cmip-00
Proxy Mobile IP (network) based
  Fabio Giust, Antonio de la Oliva, Carlos J. Bernardos, Rui Costa, “A Network-based Localized Mobility Solution for Distributed Mobility Management”, International Workshop on Mobility Management for Flat Networks (MMFN 2011)
  draft-bernardos-mext-dmm-pmip-01

## Slide 5: Introduction (I)
Network based DMM approach based on Proxy Mobile IPv6
Mobility management pushed to the edge of the network (access router level)
Two approaches explored
  Fully distributed
  Partially distributed
    Centralized control plane kind-of LMA
    Distributed data plane

## Slide 6: Introduction (II)
Mobility operations are spread among edge routers, called Mobility Anchor and Access Routers (MAARs)
  One IP hop distance from the MN
  Concentrates AR, LMA and MAG functionalities on a per-MN, per-prefix basis
  Delegates and anchors an IP prefix to each MN attached
    Serving MAAR (S-MAAR): MAAR which the MN is currently attached to
    Anchor MAAR (A-MAAR): previously visited MAAR anchoring a prefix used by an active flow of the MN

## Slide 7: Introduction (III)
Central Mobility Database (CMD): Node storing the BCE of all the MNs of the domain
  It plays the role of the LMA for the control plane
Solution in a nutshell:
  Only data forwarding is distributed
  The MAARs are the entities at the edge handling the data forwarding
  The CMD is a central node keeping track of the mobility sessions of all the MNs
  MNs get (and may keep reachable) an IP address at each MAAR they attached to

## Slide 8: Initial registration (I)
When the MN is detected by a MAAR (S-MAAR), it sends a PBU to the CMD
PBU:
    MN-ID option
    HNP option (Pref1)
  Upon reception, the CMD:
    Checks if a BCE for the MN exists:
      Not yet
    Creates one
      MN-ID => Pref1  PCoA=MAAR1
PBA:
    MN-ID
    HNP option (Pref1)
  Upon reception, the MAAR1:
    (Adds a route to the prefix: MN-ID => Pref1  on-link)

## Slide 9: Initial registration (II)
Very similar to Proxy Mobile IPv6
  Only the routing state differs:
    The CMD does not perform any MN’s data packet forwarding
    MAAR1 sets up only a downlink route
It takes one RTTMAAR-CMD for the registration

## Slide 10: Handover: 1st approach (I) (The CMD is a relay for the mobility signaling)
PBU:
    MN-ID option
    HNP option (Pref2)
  Upon reception, the CMD:
    Checks if a BCE for the MN exists:
      MN-ID => Pref1  PCoA=MAAR1
    Updates the BCE:
      MN-ID => Pref2  PCoA=MAAR2
    Sends a PBU* to MAAR1
PBU*:
    MN-ID option
    HNP option (Pref1)
    Alternate CoA option (MAAR2’s address)
  Upon reception, the MAAR1:
    Sets up a tunnel with endpoints MAAR1 and MAAR2
    Adds a route: MN-ID => Pref1  via tunnel
    Replies to CMD with a PBA

## Slide 11: Handover: 1st approach (II) (The CMD is a relay for the mobility signaling)
PBA:
    MN-ID option
    HNP option (Pref1)
  Upon reception, the CMD:
    Updates BCE:
      MN-ID => Pref2  PCoA=MAAR2
      MN-ID => Pref1  Old-PCoA=MAAR1
    Sends a PBA* to MAAR2
PBA*:
    MN-ID option
    HNP option (Pref2)
    New options (Pref1 + MAAR1’s address)
  Upon reception, the MAAR2:
    (Adds a route to the prefix: MN-ID => Pref2  on-link)
    Sets up a tunnel with endpoints MAAR1 and MAAR2
    Adds a source-route: MN-ID => from Pref1  via tunnel

## Slide 12: Handover: 1st approach (III) (The CMD is a relay for the mobility signaling)
The CMD informs the old MAAR about the new MN location (new MAAR’s address)
  Alternate CoA option
It is needed to define a new mobility option
  Required to inform the new MAAR about old MAAR address and the prefix associated to it
It takes 2 RTTMAAR-CMD to register the new location

## Slide 13: Handover: 2nd approach (I) (The CMD is used as a MAAR locator)
PBU:
    MN-ID option
    HNP option (Pref2)
  Upon reception, the CMD:
    Checks if a BCE for the MN exists:
      MN-ID => Pref1  PCoA=MAAR1
    Updates BCE:
      MN-ID => Pref2  PCoA=MAAR2
    Sends a PBU* to MAAR1
PBU*:
    MN-ID option
    HNP option (Pref1)
    Alternate CoA option (MAAR2’s address)
  Upon reception, the MAAR1:
    Sets up a tunnel with endpoints MAAR1 and MAAR2
    Adds a route: MN-ID => Pref1  via tunnel
    Replies to CMD and MAAR2 with a PBA

## Slide 14: Handover: 2nd approach (II) (The CMD is used as a MAAR locator)
PBA:
    MN-ID option
    HNP option (Pref1)
  Upon reception,
    the CMD:
      Updates BCE:
        MN-ID => Pref2  PCoA=MAAR2
        MN-ID => Pref1  Old-PCoA=MAAR1
    the MAAR2:
      (Adds a route to the prefix: MN-ID => Pref2  on-link)
      Sets up a tunnel with endpoints MAAR1 and MAAR2
      Adds a source-route: MN-ID => from Pref1  via tunnel

## Slide 15: Handover: 2nd approach (III) (The CMD is used as a MAAR locator)
The old MAAR informs about the new MN location (new MAAR’s address)
  Alternate CoA option
No need to define a new mobility option
It takes 1 RTTMAAR-CMD and ½ 1 RTTMAAR-MAAR to register the new location

## Slide 16: Handover: 3rd approach (I) (The CMD is used as a proxy)
PBU:
    MN-ID option
    HNP option (Pref2)
  Upon reception, the CMD:
    Checks if a BCE for the MN exists:
      MN-ID => Pref1  PCoA=MAAR1
    Updates BCE:
      MN-ID => Pref2  PCoA=MAAR2
    Sends a PBA* to MAAR2 and a PBU* to MAAR1
PBA*:
    MN-ID option
    HNP option (Pref2)
    New option (Pref1 + MAAR1’s address)
  Upon reception, the MAAR2
    (Adds a route to the prefix: MN-ID => Pref2  on-link)
    Sets up a tunnel with endpoints MAAR1 and MAAR2
    Adds a source-route: MN-ID => from Pref1  via tunnel

## Slide 17: Handover: 3rd approach (II) (The CMD is used as a proxy)
PBU*:
    MN-ID option
    HNP option (Pref1)
    Alternate CoA option (MAAR2’s address)
  Upon reception, the MAAR1:
    Sets up a tunnel with endpoints MAAR1 and MAAR2
    Adds a route: MN-ID => Pref1  via tunnel
    Replies to CMD
PBA:
    MN-ID option
    HNP option (Pref1)
  Upon reception, the CMD:
    Updates BCE:
      MN-ID => Pref2  PCoA=MAAR2
      MN-ID => Pref1  Old-PCoA=MAAR1

## Slide 18: Handover: 3rd approach (III) (The CMD is used as a proxy)
The old MAAR informs about the new MN location (new MAAR’s address)
  Alternate CoA option
It is needed to define a new mobility option
  Required to inform the new MAAR about old MAAR address and the prefix associated to it
It takes 1 RTTMAAR-CMD to register the new location (the CMD sends the message at the same time to the old and new MAARs)

## Slide 19: Conclusions
3 different approaches proposed
  Some require new options to be defined
  The CMD is not just a forwarder of signaling
  Different handover latencies
HO latency

## Slide 20: Questions?