## Slide 1: LISP Mobile-Node draft-meyer-lisp-mn-05.txt Chris White, Darrel Lewis, Dave Meyer, Dino Farinacci cisco Systems
EID: dino@cisco.com
RLOC: IRTF MobOpts – Quebec City
July 28 2011
Notes: <number>

## Slide 2: What if . . .
A mobile device could be server?
A mobile device did not depend on any carrier?
A mobile device could roam across different types of radios without dropping sessions?
Each mobile device keeps the same IP address no matter where goes?
LISP-MN for MobOpts
IETF/IRTF
Slide <number>

## Slide 3: Agenda
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
Why Locator/ID Separation
What is LISP?
What is LISP-MN?
Implementation Details
Futures
Notes: <number>

## Slide 4: Today – No ID/Locator Separation
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
chambers.cisco.com
Is this John at the location ‘cisco’?
Is this John at location ‘home’?
Is this John at ‘Starbucks’?
If I have a connection to John does it break because he changed locations?
198.133.219.25
Application ID
Network Location
Network ID

## Slide 5: Future – With ID/Locator Separation
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
The service binds to an Application Name (DNS)
The Application Name binds to a Endpoint ID (EID)
The EID binds dynamically to a Routing Locator (RLOC)
chambers.cisco.com
198.133.219.25
DNS Name
RLOC
EID
64.100.100.1
static binding
Provided by the DNS system
dynamic binding
Provided by the LISP routing system
Users use DNS names (the human “who”)
Applications use EIDs (the network “who”)
Routing uses RLOCs (the network “where”)

## Slide 6: What is LISP?
A new addressing architecture and protocol suite
  For separating End-point IDs and Locators
Network-based solution
No changes to hosts whatsoever
No addressing changes to site and core devices
Very few configuration file changes
Imperative to be incrementally deployable
Address family agnostic
LISP-MN for MobOpts
IETF/IRTF
Slide <number>

## Slide 7: What is LISP?
LISP is completely open
  Started in the IRTF
  Currently has an IETF working group
  No known IPR
100s of Researchers and Operators Contributed to Design
Multiple Vendors Interested
Pilot Network up for nearly 4 years
  121 nodes in 25 countries
Building a LISP-MN Pilot Network
  Testing server capabilities on Android phones
  Experimenting new mapping database systems and security mechanisms
LISP-MN for MobOpts
IETF/IRTF
Slide <number>

## Slide 8: Data-Plane Flow
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
Provider A
10.0.0.0/8
Provider B
11.0.0.0/8
S
ITR
D
ITR
ETR
ETR
Provider Y
13.0.0.0/8
Provider X
12.0.0.0/8
S1
S2
D1
D2
PI EID-prefix 1.0.0.0/8
PI EID-prefix 2.0.0.0/8
DNS entry:
D.abc.com A 2.0.0.2
EID-prefix: 2.0.0.0/8
Locator-set:
12.0.0.2, priority: 1, weight: 50 (D1)
13.0.0.2, priority: 1, weight: 50 (D2)
Mapping
Entry
1.0.0.1 -> 2.0.0.2
1.0.0.1 -> 2.0.0.2
11.0.0.1 -> 12.0.0.2
1.0.0.1 -> 2.0.0.2
11.0.0.1 -> 12.0.0.2
1.0.0.1 -> 2.0.0.2
12.0.0.2
13.0.0.2
10.0.0.1
11.0.0.1
Policy controlled
by destination site

## Slide 9: Mapping Database System
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
ETR
ETR
ALT
ALT
LISP-ALT
BGP-over-GRE
MS
MS
ALT
ALT
MS
MS
MR
MR
ALT
ALT
MR
MR
ETR
ETR
ITR
ITR
ITR
ITR
Map-Request -->
<-- Map-Request
ALT
ALT
ETR
ETR
Map-Register
Map-Register
Map-Register
10.0.0.0/8 -> (1.1.1.1, 2.2.2.2)
Database Mapping Entry:
11.0.0.0/8 -> (3.3.3.3, 4.4.4.4)
Database Mapping Entry:
Map-Request
10.0.0.1
Map-Reply
10.0.0.0/8 -> (1.1.1.1, 2.2.2.2)
10.0.0.0/8 -> (1.1.1.1, 2.2.2.2)
Mapping Cache Entry:
Map-Servers
Map-Servers
Map-Resolvers
Map-Resolvers
Map-Request
10.0.0.1
12.0.0.0/8 -> (5.5.5.5, 6.6.6.6)
Database Mapping Entry:
Map-Request
|
|
v
Map-Request
|
|
v

## Slide 10: A Multi-Homed LISP Site
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
RLOC A
RLOC A’
A’
A
EID-prefix

## Slide 11: Relationship between EIDs and RLOCs
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
Use-Case | EID | RLOC | Description
Standard Site | Static | Static | ETRs staticly configured
VM Mobility | Dynamic | Static | xTRs discover “dynamic-EIDs”
LISP-MN | Static | Dynamic | EID latched to device while radios get DHCPable “dynamic-RLOCs”

## Slide 12: LISP Hand-Set Mobility
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
3G/4G Network
WiFi Network
EID: 2610:00d0:xxxx::1/128
64.0.0.1
65.0.0.1
dynamic RLOCs
static EID
dino.cisco.com
This phone is a LISP site!

## Slide 13: LISP Mobile-Node Mobility
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
64.0.0.1
65.0.0.1
wifi
3G
(1) 2 MNs can roam and stay connected
(2) MNs can be servers
(3) MNs roam without changing DNS entries
(4) MNs can use multiple interfaces
(5) MNs can control ingress packet policy
(6) Faster hand-offs
(7) Low battery use by MS proxy-replying
(8) And most importantly, packets have stretch of 1 so latency is best for delay sensitive applications
LISP-MN can scale to 1 billion hand-sets!
Map-Server: 64.1.1.1
EID-prefix: 2610:00d0:xxxx::1/128

## Slide 14: Implementation Details
Android and Linux LISP-MN available
  Supports IPv4 or IPv6 EIDs
Design Goals
  Minimize direct kernel changes
  Architect for robustness
  Minimize network stack complexity
  Code for flexibility
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
Notes: Minimize direct kernel changes: use netfilter API to hook into IP stack without modifying an IP stack code. Use netlink API for kernel/user-level communication. Implement as loadable kernel module.
Architect for robustness: Put only what is required for the data-plane in the kernel. All else goes in user-level daemon.
Minimize network stack complexity: No virtual network device driver, no modifications to transport-layer protocols. Uses normal routing table to achieve EID address sourcing, encapsulation escape on local network.
Code for flexibility: hooks for ipv6 as we go along, underlying table API abstracted away, simple and extensible message passing between kernel and daemon.
<number>

## Slide 15: Futures
Faster Handoffs
Add LISP-SEC to LISP-MN
Use Geo Coordinates for RLOC selection
More multi-homing capabilities
LISP-MN roaming in and out of LISP sites
LISP-MN with NAT-Traversal
Augment pilot network for LISP-MN
  Experiment with concurrent end-point roaming
  Experiment with new mapping database systems
LISP-MN for MobOpts
IETF/IRTF
Slide <number>

## Slide 16: LISP is here now!
LISP-MN for MobOpts
IETF/IRTF
Slide <number>
With real implementation experience!
With real deployment experience!
With real customer engagement!
Has been that way for several years
http://www.lisp{4,6}.net
http://lisp.cisco.com
lisp@ietf.org
lisp-support@cisco.com