## Slide 1: draft-rkhd-mpls-tp-sd-03
IETF 81 Jul 2011
Rafi Ram (rafir@orckit.com)
Daniel Cohn (danielc@orckit.com)
Masahiro Daikoku (ms-daikoku@kddi.com)
Ma Yuxia (ma.yuxia@zte.com.cn)
Yang Jian (yang.jian@zte.com.cn)
Alessandro D’Alessandro (alessandro.dalessandro@telecomitalia.it)

## Slide 2: Background
This draft provides guidelines for signal degrade fault condition detection
  SD is a trigger for transport path (LSP, PW) protection
  SD detection from server/sub-layer MEP
Proposes using MPLS-TP OAM message to indicate SD condition detection

## Slide 3: Updates (1)
Change intended status to informational
Changed LSP references to “transport path”
Added text to explain that common purpose of the SD detection guidelines is that SD should reflect physical error conditions (e.g. low rx power, dispersion, bad connections), rather than non-physical error conditions (e.g. congestion, CPU overload)

## Slide 4: Updates (2)
New SD detection guidelines
  Signal degrade conditions MUST be monitored by the lowest server layer or sub-layer that is not terminated between monitoring points
  Method for determining signal degrade SHOULD allow to localize links that contribute to signal degrade
  Method for determining signal degrade MUST be able to exit signal degrade condition when error rate returns to normal condition
  Method for determining signal degrade condition MUST be scalable
Minor changes to other SD detection guidelines

## Slide 5: Updates (3)
Consider a scenario where the lower-layer BER in each link traversed by the transport path is below the SD threshold, but the accumulated BER is above the threshold
  Relevant for lower-layer technologies where errored information is discarded (e.g. Ethernet)
To support SD detection in these scenarios, nodes detecting high error rate MAY optionally include measured BER in link degradation fault messages
Transport path client MEP declares SD based on the sum of received BER values

## Slide 6: Updates (4)
Recommend using encapsulation and mechanism defined in draft-ietf-mpls-tp-fault to send link degradation fault indication when SD is detected

## Slide 7: Next Steps
Incorporate input into next draft
Define format and encapsulation of link degradation fault indication, based on draft-ietf-mpls-tp-fault
Request working group adoption

## Slide 8: Thank You
Questions ? Comments ?