## Slide 1: draft-ali-mpls-inter-domain-p2mp-rsvp-te-lsp-06.txt MPLS WG IETF-81 Quebec City, Canada July, 2011
Presenter: Rakesh Gandhi
Authors: Zafar Ali, Rakesh Gandhi
zali@cisco.com, rgandhi@cisco.com
Notes: <number>

## Slide 2: Agenda
Inter-domain P2MP-TE - Problem Statement
RFC 4875 - P2MP-TE Remerge Handling
Control-plane Method
Data-plane Method
Next Steps
Notes: <number>

## Slide 3: Inter-domain P2MP-TE - Problem Statement
One requirement for P2MP-TE LSP is to avoid re-merges as these are inefficient and result in duplication of traffic
The term "re-merge" refers to the situation when two S2L sub-LSPs branch at some point in the P2MP-TE Tree, and then merge back at another downstream node
In case of inter-domain P2MP-TE LSP, re-merges can happen as different border nodes performing loose-hop ERO expansions do not have knowledge of the entire P2MP-TE LSP
RFC4875 (RSVP-TE extensions for P2MP-TE) does not address inter-domain requirements
RFC5151 (Inter-domain RSVP-TE extensions) does not address P2MP-TE
RFC4920 (Crankback signaling extensions) does not address P2MP-TE signaling
Notes: <number>

## Slide 4: RFC 4875 - P2MP-TE Remerge Handling
RFC 4875 specifies two methods to handle P2MP-TE re-merge conditions:
Control plane method: the re-merge node initiates the removal of the re-merge branch(es) by sending a Path Error message.
Data plane method: the re-merge node allows the re-merge to persist, but data from all but one incoming interface is dropped at the node. This ensures that duplicate data is not sent on any outgoing interface.
Notes: <number>

## Slide 5: Control-plane Method Extension
Ingress selects the same domain border node for ERO expansion for all siblings transiting a given domain. Domain border nodes expand EROs for all siblings S2L such that the overall path taken by these siblings in the domain is remerge free.
Crankback Signaling:
  Crankback procedures defined in RFC 4920 can be applied to P2MP-TE LSPs to handle re-merge conditions.
  Does not require selection of same domain border node for all siblings transiting a given domain.
  For siblings that have failed the LSP setup, on receipt of a Path Error a domain border node may hold the Path Error for re-merge.
  The domain border node may try to signal an alternate path through the domain, for siblings that have failed the LSP setup.
  If a subsequent attempt is successful, the domain border node discards the held Path Error message.
  If all subsequent attempts are unsuccessful, the domain border node forwards the Path Error to the head-end node.
Notes: <number>

## Slide 6: Data-plane Method Extension - Path Message
In order to indicate transit nodes that P2MP-TE Re-merge Recording is requested, a new flag in the Attribute Flags TLV of the LSP_ATTRIBUTES object defined in [RFC 5420] is defined as follows:
Bit Number (to be assigned by IANA): P2MP-TE Re-merge Recording Request flag
The P2MP-TE Remerge Recording Request flag is meaningful on a Path message and can be inserted by the ingress node or a border node that understands the P2MP-TE Re-merge Present Flag (next slide) in RRO Attributes Sub-object.
Notes: <number>

## Slide 7: Data-plane Method Extension - Resv Message
When a node understands the "P2MP-TE Re-merge Recording Request” in the Attribute Flags TLV of the LSP_ATTRIBUTES object of the Path message, the node SHOULD set the newly defined "P2MP-TE Re-merge Present" flag in the RRO Attributes sub-object defined in [RFC 5420] in RRO:
Bit Number (same bit number assigned for P2MP-TE Re-merge Recording Request flag): P2MP-TE Re-merge Present flag
The presence of P2MP-TE Re-merge Present flag indicates that the S2L is causing a re-merge. The re-merge has been accepted but the incoming traffic on this S2L is dropped by the reporting node.
Proposed extension allows a border node and/or a head-end to optimize bandwidth at some later time in future while immediately starting the traffic to all possible destinations of the inter-area P2MP-TE LSP
Notes: <number>

## Slide 8: Next Steps
We would like to make this document a WG Document.
Notes: <number>

## Slide 9
Thank You.
Notes: <number>

## Slide 10: P2MP-TE Remerge
B19
C
S
D
B23
B22
B21
B1
B2
D2
B24
D1
H
B26
B20
B16
J
B15
B17
G
B18
RSVP-TE signaling based solutions to address these requirements are not defined in RFC4875.
The above mentioned situation can even lead to infinite signaling loop, some destinations will never receive traffic.
ERO-L (D1)
ERO-L (D2)
Remerge happens at (C) in domain 3
Domain 1
Domain 2
Domain 3
Domain 4
Notes: <number>