## Slide 1: Targeted mLDP
  Base mLDP spec didn’t consider use of LDP multipoint extensions over Targeted mLDP sessions
    LDP speaker must choose “upstream LSR”, i.e., next hop on path to root of MP LSP being constructed
    Only IGP next hop considered, assumes upstream LSR is IGP neighbor
  Targeted mLDP can be useful way of applying LSP hierarchy to MP LSPs
  Draft-napierala-targeted-mldp specifies use of MP extensions on targeted LDP sessions

## Slide 2: Hierarchical Topology
Egress (Downstream) Ingress (Upstream)
PE1---ABR1
(Backbone) ABR3---PE3
PE2---ABR2
ABRs not IGP adjacencies, but are LDP peers over targeted sessions
(Sorry about the ASCII Art)

## Slide 3: Approach
  No new protocol, messages, or TLVs
  Adds procedures to enable:
    LDP speaker to select peer over targeted session as “upstream LSR”
    Upstream LSR to transmit data through tunnel(s) to downstream LSRs
      Ingress replication (through unicast tunnels), or
      Multicast tunnels
        Optional aggregation through use of upstream-assigned labels

## Slide 4: Ways of Choosing Upstream LSR
  Suppose ABRs 1 and 2 need to create P2MP-LSP with root PE3
  ABR1 can choose ABR3 as upstream LSR on path to PE3 if:
    ABR3 is BGP next hop on ABR1’s path to PE2, or
    Backbone is full mesh of P2P TE tunnels, ABR3 is head of ABR1’s next hop interface (tunnel) to PE2
    IGP tells ABR1 that ABR3 is the border router on its path to PE2
  Similarly, ABR2 may choose ABR3 as upstream LSR

## Slide 5: Ingress Replication over Backbone
ABR1 and ABR2 send Label Mapping Messages to ABR3
  Include downstream-assigned “multicast label’ representing the P2MP LSP
  ABR3 makes two copies of data, unicasts one to ABR1 and one to ABR2
  Each packet carries two labels, e.g:
  Unicast label for ABR1
  ABR1’s multicast label
  Data

## Slide 6: Multicast Tunnels over Backbone
ABR1 and ABR2 send Label Request Messages to ABR3
ABR3 sends Label Mapping Messages to ABR1 and ABR2
  Uses procedures from draft-ietf-mpls-ldp-upstream (on RFC Editor’s queue)
  Include Interface TLV, specifying multicast tunnel, and (optionally) upstream-assigned label for aggregating several MP LSPs inside single tunnel
    Tunnels can be TE P2MP, e.g.

## Slide 7: Summary
  Straightforwardly extends multipoint extensions to case of targeted LDP
  No new protocol
  Allows hierarchy to be applied in a manner that is transparent to the ingress and egress Pes
  Supports multiple backbone transmission schemes and allows aggregation
  Seems non-controversial … 