## Slide 1: 1:n protection for MPLS-TP
draft-ezy-mpls-1toN-protection
eosborne@cisco.com
zhang.fei3@zte.com.cn
yaacov.weingarten@nsn.com

## Slide 2: Agenda
Overview
Motivation
Open question
Next steps

## Slide 3: Overview
1:1/1+1 PSC exists, almost RFC (draft-ietf-mpls-tp-linear-protection)
Provides messaging to coordinate protection state at two ends of a protection domain, similar to APS/G.8031
This draft extends PSC to support 1:n
  Adds necessary pieces for 2-phase support

## Slide 4: Motivation
1:1/1+1 PSC is progressing through final reviews before becoming an RFC
1:n is required per rfc5654 R67 (2.5.1.1)

## Slide 5: Open question
1:1/1+1 is single-phase
1:n must be multiphase
  Needs to ensure both ends of the protection domain are protecting the same thing

## Slide 6: Open question
In traditional transport networks, switch acts as a lock (cannot send newly protected traffic until the 2-phase operation is complete).
  Necessary because the payload could be misconnected
In traditional MPLS-TE networks, no need to use switch operation as a lock
  Payload beneath W or P LSP label is a label the Rx node already knows
  Rx node will always have an ILM entry for a label stack and thus will never misconnect
  Interim asymmetric protection means at least there’s some protection

## Slide 7: Two-phase with lock
Traffic is flowing
No traffic on P
(1xRTT traffic loss)
W4 fails
SF(4,0)
Ack (4,4)
SF(4,4)
Traffic starts flowing again

## Slide 8: Two-phase without lock
Traffic is flowing
W4 payload
immediately sent
on P (no loss)
W4 fails
SF(4,0)
Ack (4,0)
SF(4,4)

## Slide 9: Open question
Are there scenarios where a lock is necessary?
(would like to discuss on the list)

## Slide 10: Next steps
Comments welcome
WG draft?