## Slide 1: IETF 81 – Quebec City July 2011
LDP Outbound Label Filtering
(draft-raza-mpls-ldp-olf-00.txt)
Kamran Raza
Sami Boutros
Pradosh Mohapatra
(Cisco Systems, Inc.)

## Slide 2: Problem
In Downstream Unsolicited label advertisement mode, an LDP speaker LSR1 may receive label bindings from peer LSR2 for the FECs in which it has no interest.
The label bindings are sent by the peer LSR2, received at the LDP speaker LSR1, and then discarded.
This is wasteful from resource point of view:
  Sender LSR resources
  Network resources
  Receiver LSR resources

## Slide 3: Solution: Receiver-pushed OLF Policy at Sender
One possible solution is to use DoD mode:
  Solicit label bindings from peer for interesting FECs only.
  The drawbacks:
    DoD mode mandated for both LSRs though it’s really required by one of them.
    Slower convergence compared to DU mode.
This draft proposes an alternative solution:
  Receiver LSR1 pushes its label policy to sender LSR2 that LSR2 applies before sending FEC-label bindings towards LSR1.
  Label policy is pushed/applied for initial updates as well as updated dynamically.

## Slide 4: Operational Examples
LSR with limited LIB space
  Use OLF framework to initially disable all label binding exchange at the peer side, and then selectively allow FEC via OLF filter updates sent to peer
Label Filtering at ABRs
  ABR1 (backbone and non-zero areas) LDP speaker may advertise bindings for prefixes from all area, when ABR2 LDP requires bindings only for backbone area prefixes.
  Use OLF mechanisms to filter unnecessary prefix label bindings towards ABR2 at ABR1.

## Slide 5: OLF Mechanism
LSRs exchange “OLF Capability” to announce their capability to send or receive label policy filters. The capability can be:
  announced at session establishment time in LDP Initialization message
  announced/withdrawn dynamically during session life time if LSRs support “Dynamic Capability Announcement” capability.
After capability negotiation, the label policy and its update is sent in an LDP Notification message with new “OLF Status”.
  No “incremental” updates – new filter replaces previous filter.
  Post Capability negotiation:
    “receive” capable LSR: No FEC-label bindings sent to peer and wait for policy message
    “send” capable LSR: Push its label policy filter to peer.
  Label Policy update:
    “send” capable LSR: Constructs OLF filter according to local policy and push to peer.
    “receive” capable LSR: Applies received OLF filter and announces/withdraws label bindings accordingly from the peer.

## Slide 6: OLF Mechanism (2)
The OLF capability negotiation, and the policy updates are performed, for a given FEC type.
  The actual format of a policy filter and its matching rules are FEC-dependent and are to be specified by FEC designers.
  This document specifies the format and matching rules of policy filter for “Address Prefix” FEC type.

## Slide 7: OLF Policy Framework
Constructs:
  OLF-Policy: <OLF-Elements>
  OLF-Element: <FEC-Type> <OLF-Entries>
    FEC-Type: <FEC Element Type, Address Family>
  OLF-Entry: <Action, OLF-value>
    Action: PERMIT, DENY, PERMIT-ALL
    OLF-value: FEC-specific component and provides the specification of FEC for matching.
Rules for OLF Element/Entry:
  If Action=PERMIT-ALL, no OLF-value component specified.
  For an OLF Element containing more than one OLF entry, the receiving LSR MUST process the OLF entries in the same order as they are specified inside the OLF element.
  Each OLF Element has an *implicit* DENY-ALL as the last rule
    The sender and the receiver of OLF policy to keep this in mind in constructing/processing an OLF filter respectively.

## Slide 8: Signaling: OLF Capability
OLF Capability TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|0| OLF Capability(IANA) | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|S| Reserved | |
+-+-+-+-+-+-+-+-+ |
| |
~ OLF Capability Element(s) ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++-+-+-+-+-+-++-+-+-+-+-+-+-+
S=1/0 to announce/withdraw the capability
OLF Capability Element
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| FEC Elem Type | Address Family |T|R| Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
T: OLF Send capable, R: OLF Receive capable
An LDP speaker that advertises OLF capability MUST support "OLF Policy Status" and "OLF Status" Status Code.

## Slide 9: Signaling: OLF Policy
OLF policy is signaled to a peer through LDP Notification messages, where LDP status code is set to “OLF Status” and OLF specs are carried in new status TLV “OLF Policy Status”
Sample OLF-Policy: [OLF-Policy-Status] <Length>
    [OLF-Element1] <FEC-Elem1><AF1><Length> [OLF-Entry1] <Action><OLF-value11>
    [OLF-Entry2] <Action><OLF-value12>
    [OLF-Element2] <FEC-Elem2><AF2><Length>
    [OLF-Entry1] <Action><OLF-value21>
    [OLF-Entry2] <Action><OLF-value22>
OLF Policy Status TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|U|F| OLF Policy Status(IANA) | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|M| Reserved | |
+-+-+-+-+-+-+-+-+ |
~ OLF Element(s) ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++-+-+-+-+-+-++-+-+-+-+-+-+-+
M=“More” bit to indicate if this is partial policy update or end of current update.

## Slide 10: Signaling: OLF Policy (2)
OLF Element
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| FEC-Elem-Type | Address-Family | Length ... |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ... | |
+-+-+-+-+-+-+-+-+ |
~ OLF Entries ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++-+-+-+-+-+-++-+-+-+-+-+-+-+
OLF Entry
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Common part | |
+-+-+-+-+-+-+-+-+ |
~ Type-specific part ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++-+-+-+-+-+-++-+-+-+-+-+-+-+
where Common part is
0 1 2 3 4 5 6 7
+-+-+-+-+-+-+-+-+
|Action | Rsvd |
+-+-+-+-+-+-+-+-+

## Slide 11: “Address Prefix” FEC OLF Entry
FEC-Type:
  FEC-Elem-Type: 0x2 ("Address Prefix")
  Address-Family: 1 (IPv4) or 2 (IPv6)
  Address Prefix FEC OLF Entry
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Action | Rsvd | Minlen | Maxlen | Prefix Len |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ Prefix ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++-+-+-+-+-+-++-+-+-+-+-+-+-+
Where:
The "Minlen" and "Maxlen" fields indicate respectively the minimum and the maximum prefix length used for "matching”

## Slide 12: “Address Prefix” FEC OLF Entry
Address Prefix OLF Entry Matching rules:
If route prefix is neither more specific than, nor equal to, the <Prefix, Prefix Len> fields of the OLF entry: then it is “NO MATCH”,
Else: the route is considered as a MATCH to the OLF entry only IF following match conditions are met:
OLF Entry Route Prefix
Minlen Maxlen Match Condition
+------------------------------------------------------------------+
| un-spec. | un-spec. | Route.Prefix Len == OLF.Prefix Len |
| specified | un-spec. | Route.Prefix Len >= OLF.Minlen |
| un-spec. | specified | Route.Prefix Len <= OLF.Maxlen |
| specified | specified | Route.Prefix Len >= OLF.Minlen |
| | | AND Route.Prefix Len <= OLF.Maxlen |
+------------------------------------------------------------------+
Sample Filter:
    Prefix-IPv4 Permit: [1.1.1.0/24; minlen=31, maxlen=32] Permit: [2.2.2.2/32; minlen=32, maxlen=32] Deny: [3.3.3.0/24; minlen=31, maxlen=32] Permit: [3.3.3.0/24; minlen=24, maxlen=32] Prefix-IPv6 Permit-All

## Slide 13: I-D Status
Open Items:
  Change title: LDP Outbound Label Bindings Filtering
  Provision for OLF filter/policy incremental updates ?
Next Steps:
  Seeking feedback
  Looking for WG adoption
Acknowledgments:
  BGP ORF: RFC5291, RFC5292
  Eric Rosen