## Slide 1: draft-ietf-mpls-lsp-ping-mpls-tp-oam-conf-02 Configuration of Pro-Active Operations, Administration, and Maintenance (OAM) Functions for MPLS-based Transport Networks using LSP Ping
E. Bellagamba, Ericsson
P. Sköldström, Acreo
D. Ward, Juniper
J. Drake, Juniper
L. Andersson, Ericsson

## Slide 2: Overview
To specify the mechanisms necessary to establish MPLS-TP OAM entities monitoring an LSP and define information elements and procedures to configure pro-active MPLS OAM functions.
OBJECTIVE
Previous
Version
Configuration via LSP-PING of:
BFD CC and CV
Performance Monitoring Loss
Performance Monitoring Delay
Fault Management Signal

## Slide 3: Changes respect to the previous version [1]
Major changes in the following sections in order to de-emphasize BFD and have the same visibility for the whole set of tools:
  Section 1 – Introduction
  Section 2 – Overview of MPLS OAM
  Section 3 - Theory of Operations
Changes in BFD configuration:
  CC&CV functions are now part of the same functionality, it is not possible anymore to activate them separately
  Detect Multiplier has been deleted from the configurable parameters because it has been fixed to value 3 in draft-ietf-mpls-tp-cc-cv-rdi-05
  Encapsulation capability flags: allow to set either G-ACh encapsulation or UDP encapsulation
  Bidirectional/Unidirectional flag

## Slide 4: Changes respect to the previous version [2]
New “Performance Monitoring TLV” in order to allow configuration flags for Loss, Delay and Throughput Measurements that can’t be handled in the corresponding sub-TLVs. Such flags are aligned with draft-ietf-mpls-loss-delay-04
D: Delay Inferred/Direct
L: Loss Inferred/Direct
J: Delay variation/jitter
Y: Dyadic
K: Loopback
C: Combined
Loss and Delay TLV are now sub-TLV of the new Performance monitoring TLV
Loss and Delay sub-TLVs have been updated in order to conform to the new version of draft-ietf-mpls-loss-delay-04

## Slide 5: Next Steps
The current version address comments from the authors of:
  draft-ietf-mpls-loss-delay
  draft-ietf-mpls-tp-cc-cv-rdi-05
Continue keeping the three configuration drafts aligned
  draft-ietf-mpls-lsp-ping-mpls-tp-oam-conf
  draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
  draft-zhang-mpls-tp-pw-oam-config (configuration for PW)
Authors think the document it is ready for last call