## Slide 1: MPLS WG
Extensions to RSVP-TE for Bi-directional Label Switched Paths (LSPs)
Notes: <number>

## Slide 2: Motivation
Symmetrical MPLS-TE path application:
  IEEE-1588 which requires that the Delay_Req message takes the same path as the associated Sync message.

## Slide 3: Current State
MPLS LSPs are Unidirectional - Separate LSPs are required for bi-directional traffic flow
GMPLS has defined extensions for setting up bi-directional LSPs
Draft uses the GMPLS extensions and applies those to regular MPLS LSPs and also discusses how bi-directional symmetrical FRR can be achieved
Notes: <number>

## Slide 4: Setting up the RSVP-TE Bi-Directional LSP
Use Upstream_Label object in the PATH message.
When an MPLS node desires label recording, it adds this Upstream Label in the RRO sub-object in PATH message:
  Thus the initial RRO will now contain the sender's IP address and the Upstream Label advertised by it.
  Upstream label subobject: type 0x04 and same C-type with label object.
Notes: <number>

## Slide 5: FRR Mechanisms
Head-end A
G
Tail-end E
F
C
D
B
B is the PLR for traffic in one direction
D is the PLR and B the MP for traffic in reverse direction
ABCDE - Protected bi-directional LSP
BFGD - Bi-directional bypass tunnel for protecting node C
Downstream PLR
Downstream MP
Upstream PLR
Upstream MP
Notes: <number>

## Slide 6: Bi-directional By-Pass tunnel
Protected bi-directional LSP -> bi-directional detour and bypass tunnels.
  Uses the same Upstream_label mechanism that was used to set up the bi-directional LSP
Upstream PLR learns the incoming labels expected by its downstream routers by examining the RRO in the RESV messages
Downstream PLR for the reverse direction, learns the Upstream labels by examining the RRO in the PATH message
Notes: <number>

## Slide 7: Failure Detection between PLR and MP
Its required that the PLR and MP detect the failure at the same time so that they switch to the bypass or the detour tunnel at the same time
  We could use BFD, RSVP-TE Hello, or some other mechanism for this.
  We suggests using BFD - more details in the draft.
Alternate mechanism is to do protected LSP segment detection between the PLR and the MP.
Notes: <number>

## Slide 8: Next steps
Comments and feedback of the WG?
Thank you!