## Slide 1: Handling MPLS-TP OAM Packets Targeted at Internal MIPs
draft-farrel-mpls-tp-mip-mep-map-04
H. Endo , A. Farrel, Y. Koike, M. Paul, R. Winter

## Slide 2: History
OAM framework specifies per-interface MIPs (two or more MIPs on each side of the forwarding engine)
Does not specify how OAM packets destined to per-interface MIPs are handled
  Many possible options...needs to be specified for implementors

## Slide 3: More history
Changes since -03 version
  Removed the use of ACH TLVs based on feedback received
  Removed the use of a reserved label based on feedback received
  Described (two) new way(s) of addressing per interface MIPs
  Merged with draft-koike-ietf-mpls-tp-oam-maintenance-points-01
  Appendix with ohter alternatives

## Slide 4: Requirements
Forwarding of OAM packets exactly as data packets without mis-ordering.
Delivery of OAM messages to the correct MPLS-TP node.
Direction of OAM instructions to the correct MIP within an MPLS-TP node (arrival at the wrong MIP should be handled).
Packet inspection at the incoming and outgoing interfaces must be minimized.

## Slide 5: Option 1 - Reserved bit
No semantic overlap with anything that exists
Still enough bits left (8 bits)
Potentially safe (must be ignored by legacy)
Hardware-friendly
Update to RFC 5586 and 4385, then works for both PWs and LSPs

## Slide 6
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LSP Label | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| GAL | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version| Reserved | Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ACH TLV Header (if present) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ~
~ Zero or more ACH TLVs ~
~ (if present) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ~
~ G-ACh Message ~
~ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0: ingress
1: egress

## Slide 7: Option 2 – ID-based
Use existing ID information in the OAM messages
Leave it to the node implementation to deliver it
No „on-the-wire“ packet format changes required
Slightly more complex processing compared to option 1

## Slide 8
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LSP Label | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| GAL | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version| Reserved | Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ACH TLV Header (if present) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ~
~ Zero or more ACH TLVs ~
~ (if present) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ~
~ G-ACh Message ~
~ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
ID TLV

## Slide 9: Option 2 and current solutions
draft-on-demand-cv-05 already specifies Ingress/Egress IF_Num
Address/ID TLVs
  Not a fixed location (within and across solutions) therefore a SW solution is needed
Need to make sure this solution is satisfying all of the requirements

## Slide 10: Draft-on-demand-cv-05 DSMAP/DDMAP address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MTU | Address Type | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ingress IF_Num (4 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Egress IF_Num (4 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Multipath Type| Depth Limit | Multipath Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: Next steps
Come to a conclusion on which option to pick
  Feedback please
Ensure this is safe in all conceivable cases (i.e. no OAM packet leakage)
WG adoption would be good
  Even if it‘s just to get this requirement into the back of people‘s heads
  would be standards track...or alternatively move the text into another document