## Slide 1: MPLS-TP Shared Mesh Protection draft-cheung-mpls-tp-mesh-protection-03
IETF 81 – Quebec City, July 2011
Tae-sik Cheung – cts@etri.re.kr Jeong-dong Ryoo – ryoo@etri.re.kr
Notes: <number>

## Slide 2: Motivation
MPLS-TP has requirements for shared protection in RFC5654.
  [Requirement 66] MPLS-TP must support the ability to share protection resources amongst a number of transport paths.
  [Requirement 68] MPLS-TP should support 1:n (including 1:1) shared mesh recovery.
  [Requirement 69] MPLS-TP must support sharing of protection resources.
This work proposes a shared mesh protection mechanism to meet those requirements.
Notes: <number>

## Slide 3: Shared Protection – Linear
W1
P
Wn
W1
P1
Wn
Pn
1 protection path is shared by
N working paths.
2-phase protocol should be used
to prevent misconnection.
N protection paths are dedicated
to N working paths. (Bandwidth
is shared by N protection paths.)
1-phase protocol can be used.
 Fast protection time !!
1:n architecture
(1:1)^n architecture
Notes: <number>

## Slide 4: Shared Protection – Mesh
Shared Nodes
Shared Nodes
1 protection segment is
shared by N working paths.
End-to-end protection path
cannot be established until
shared nodes are setup.
Requires 2-phase protocol.
N protection paths are
dedicated to N working paths.
End-to-end protection paths
are pre-established.
1-phase protocol is enough.
 Fast protection time !!
W1
P
Wn
W1
P1
Wn
Pn
1:n architecture
P
(1:1)^n architecture

## Slide 5: Proposed Approach (1)
The architecture is based on the (1:1)^n architecture defined in RFC4428 (GMPLS-based recovery mechanism) as well as ITU-T G.808.1 (Generic protection switching).
  End-to-end protection paths can be pre-established and monitored.
Each end node uses existing end-to-end linear protection protocol.
  This includes retransmission to handle lost messages.
  Same technique is used in MPLS-TP and Ethernet, linear and ring protection solutions.
Notes: <number>

## Slide 6: Proposed Approach (2)
The following extensions are made to the existing end-to-end linear protection:
  Notification of protection switching event to shared node
  Generation of Lockout/Clear command upon receiving lock/unlock request from shared node.
Shared node coordinates the use of protection resource.
  It compares priority assigned to each protection path.
  It sends lock/unlock request to end nodes having equal or lower priority.
Notes: <number>

## Slide 7: Operation Example
A
B
P
Q
Priority: APQB > CPQD
Shared End Node: Q
3) Initiates linear protection
switching
C
D
1) SF occurs
X
2) Sends protection state change notification messages
4) Sends protection locking messages
5) Sends LoP
[Assumptions]
Protection
Completed !!
Notes: <number>

## Slide 8: Next Steps
We need continued discussion and development on the shared mesh protection mechanism.
There are currently three I-Ds on shared mesh protection:
    draft-cheung-mpls-tp-mesh-protection
    draft-zhang-mpls-tp-shared-mesh-protection
    draft-pan-shared-mesh-protection
  The working group does not need three solutions!
  We need to analyze the different requirements driving the different solutions.
  We want to take the best ideas from all three drafts
We kindly ask the WG experts to review our document and provide us feedback.
Notes: <number>