## Slide 1: Upstream LSR Redundancy for Multi-point LDP Tunnels draft-pdutta-mpls-mldp-up-redundancy-00.txt IETF-81
Pranjal Kumar Dutta Wim Henderickx
Alcatel-Lucent

## Slide 2: Goals
Minimize the service disruption due to node/link failures when mLDP is deployed
The draft proposes a set of procedures that minimize packet loss when an upstream LSR node or link fails.
This document does not change any specifications of mLDP, no interoperability issues.

## Slide 3: Topology
Scenario 1: ECMP
Scenario 2: non-ECMP

## Slide 4: Procedures (1)
Upstream LSR failure protection can be provided by taking advantage of redundant topologies in service provider networks.
A local LSR Z selects two upstream LSRs
  One primary LSR U and at least one backup LSR U'.
  Label mappings L sent to U and L' sent to U’ shares the same downstream next-hop label forwarding entries at Z

## Slide 5: Procedures (2)
Data packets are received by Z from both U and U' simultaneously. Redundant packets received from U' are discarded by Z.
When Z detects a reachability failure to U then it switches its upstream to the backup LSR U' and packets are immediately available to forward out of each downstream next-hops.

## Slide 6: Procedures (3)
Selection of backup upstream LSR
  ECMP case
    Hash based selection of the candidate upstream LSR(s)
  Non ECMP
    LFA based selection of the candidate upstream LSR(s)

## Slide 7: Next Steps
Adding more text on failure detection/triggers
Propose to adopt this as WG document?

## Slide 8
Questions/Comments?