## Slide 1: MPLS-TP OAM ID MIB
draft-vkst-mpls-tp-oam-id-mib-00
Sam Aldrin
Tom Nadeau
Venkatesan Mahalingam
Kannan Sampath
Ping Pan
Sami Boutrous

## Slide 2: Introduction
This draft defines the identifiers for MPLS-TP LSPs, Pseudowires and sections for OAM operations.
The OAM MIB module defines following tables,
  mplsOamMegTable
  mplsOamMeTable
The new tables are generic enough to handle both the IP and/or ICC operator based TP identifiers.

## Slide 3: New Tables
MEG Table
  Manages one or more Maintenance Entities (MEs) that belongs to the same transport path
ME Table
  Defines a relationship between two points (source and sink) of a transport path to which maintenance and monitoring operations apply.
  Supports the configurations of MEP (Maintenance Entity Group End Point) and MIP (Maintenance Entity Group Intermediate Point).

## Slide 4: Why New Tables?
The new tables are used to perform the below OAM operations,
  Continuity Check and Connectivity Verification
  Remote Defect Indication
  Alarm Reporting
  Lock Reporting
  Lock Instruct
  Client Failure Indication
  Packet Loss Measurement
  Packet Delay Measurement

## Slide 5: Example
MEG Index | ME Index | MP Index | MP Type | MEP Direction | Service Pointer
1000 | 100 | 10 | mep | down | mplsTunnelName.200.1.10.20
1000 | 200 | 20 | mep | down | -
MEG Index | MEG Name | Operator Type | Service Type
1000 | LSP1 | Ipcompatible | Lsp
2000 | PW1 | Ipcompatible | pseudowire
Tunnel Index | Tunnel Instance | Ingress LSR Id | Egress LSR Id | XC Index
200 | 1 | 10 | 20 | 2
Standard MPLS Tunnel table
MPLS OAM MEG Table
MPLS OAM ME Table

## Slide 6: Next Steps
  Does the WG find this work useful and satisfying of the chartered items for MPLS-TP OAM identifier MIB modules?
    If so, we ask that the WG Accept draft-vkst-mpls-tp-oam-id-mib-00 as WG document
  Additional comments/review are requested.

## Slide 7: Thank You