## Slide 1: Incremental Label Announcement LDP GR Extensions @ IETF 81
Alton Lo (altonlo@cisco.com)
Keyur Patel (keyupate@cisco.com)
Vanson Lim (vlim@cisco.com)

## Slide 2: Motivation
LDP GR speaker re-advertise all its local bindings to all its peer upon GR restart.
By preserving all the label bindings and versioning the label binding, LDP-GR speaker should always advertise the “incremental” changes in label binding only.
By eliminating all the unnecessary retransmission of label bindings, this should reduce CPU spike and accelerate convergence.

## Slide 3: ILA Capability TLV
LDP GR Peer
ILA Capable
LDP GR Peer
ILA Capable
LDP Initialization Message Exchanged between
LDP GR Peers. ILA Extension defines a new
Capability TLV which specifies the list of
FEC Type supporting ILA.
LDP Initialization Message contains:
FT Session TLV = (0x0503)
ILA Capability TLV

## Slide 4: New ILA FEC TLV
Used for both advertisement and withdraw label bindings
Describe the FEC Type
Two Modes:
  Request Mode: initiate by LMR after restart
  Assign Mode: send by LMS in response to ILA Request Message
Version ID is 64 bits

## Slide 5: Preserve Label Bindings
Local Label Binding
Remote Label Bindings
LMS
LB1 | Version 1
LB2 | Version 2
LB1 | Version 1
LB2 | Version 2
LMR
LMS preserves its local bindings
LMR preserves the remote bindings
LDP LB1 + ILA assign Msg ver1
LDP LB2 + ILA assign Msg ver2

## Slide 6: After GR restart
Local Label Binding
Remote Label Bindings
LMS
LB1 | Version 1
LB2 | Version 2
LB3 | Version 3
LB4 | Version 4
LB1 | Version 1
LB2 | Version 2
LMR
ILA assign Message version 2
ILA request Message version 2