## Slide 1: Framework for latency and loss traffic engineering application draft-fuxh-ccamp-delay-loss-te-framework-00.txt draft-fuxh-ccamp-delay-loss-rsvp-te-ext-00.txt
Xihua Fu, Malcolm Betts, Qilei Wang ZTE
Dave McDysan, Andrew Malis Verizon
John E Drake Juniper
Spencer Giacalone Thomson Reuters
Notes: <number>

## Slide 2: Background
The key driver is stock/commodity trading and data center applications. The purpose is to make an accurate end-to-end prediction of latency and packet loss before a path is established.
Track
  draft-wang-ccamp-latency-te-metric was presented in 79th and 80th in CCAMP.
  Chairs (Lou and Acee) suggest the overlap OSPF portions of draft-wang-ccamp-latency-te-metric be combined with draft-giacalone-ospf-te-express-path
  Chairs (Lou and Ross) suggest framework and rsvp-te should be done in MPLS WG.
  Restructure the draft-wang into a framework and some protocol specific parts (e.g., OSPF and RSVP-TE) to address the issues raised in the framework.

## Slide 3: Document structure
Based on the suggestion from chairs, framework and rsvp-te documents will be renamed with title “mpls” and posted to MPLS WG.
draft-fuxh-mpls-delay-loss-te-framework-00
draft-giacalone-ospf-te-express-path-01
draft-fuxh-mpls-delay-loss-rsvp-te-ext-00

## Slide 4: Requirement Identification
Num | Requirement | Implication
REQ1 | To communicate latency, latency variation and packet loss as a link’s traffic engineering performance metric into IGP. | OSPF Extension Local Configuration
 | To control latency and loss IGP message advertisement and avoid unstable when the latency, latency variation and packet loss value changes. | 
REQ2 | Path computation entity MUST have the capability to compute one end-to-end path with latency and packet loss constraint. | Path Computation
REQ3 | To indicate a traffic flow should select a component link with minimum latency and/or packet loss value, maximum acceptable latency and/or packet loss value and maximum acceptable delay variation value | RSVP-TE Extension [CL-REQ]
REQ4 | To indicate FA selection or FA-LSP creation with minimum latency and/or packet loss value, maximum acceptable latency and/or packet loss value and maximum acceptable delay variation value. | RSVP-TE Extension
Notes: Making latency, latency variation and packet loss as a Link attribute.
Path computation with latency and packet constraint.
Component Link or FA selection/creation based on latency/packet constraint.
Latency accumulation and verification along one path across multi-domain.
Some customers may insist on having the ability to re-route or protection if the latency SLA is not being met.
Some customers may insist on having the ability to re-route to optimize latency and/or loss end-to-end cost.
<number>

## Slide 5: Requirement Identification
Num | Requirement | Implication
REQ5 | To accumulate latency of links and nodes along one LSP across multi-domain (e.g., inter-AS, inter-Area or multi-layer) so that an latency validation decision can be made at the source node. | RSVP-TE Extension
REQ6 | To support pre-defined protection or dynamic re-routing, if a "provisioned" end-to-end LSP latency and/or loss could not meet SLA anymore. | Network Planning
REQ7 | To support re-routing latency and/or loss end-to-end cost, if a “provisioned” end-to-end LSP latency and/or loss performance is improved because of some segment performance promotion. | Network Planning
REQ8 | To indicate the switchover of the LSP according to maximum acceptable change latency and packet loss value in order to avoid unstable | Local Configuration

## Slide 6: Purpose draft-fuxh-ccamp-delay-loss-rsvp-te-ext-00.txt
The RSVP-TE portions in draft-wang-ccamp-latency-te-metric is moved into this draft.
The purpose is to extend RSVP-TE protocol to promote SLA experience of latency and packet loss application in inter-AS, inter-Area or multi-layer network.
  REQ3: To facilitate the component link selection or creation based on latency and packet loss constraint.
  REQ4: To facilitate the FA selection or FA-LSP creation based on latency and packet loss constraint.
  REQ5: To accumulate latency of links and nodes along one LSP across multi-domain so that an latency validation decision can be made at the source node.

## Slide 7: Component Link or FA Selection/Creation
Latency SLA Parameters ERO subobject
  It is added into the boundary node of FA-LSP or Composite Link.
  It explicitly conveys the latency SLA parameter used for component link or FA selection and creation based on the latency constraint.
    I bit: indicates whether a traffic flow shall select a component link or FA with the minimum latency value or not.
    V bit: indicates whether a traffic flow shall select a component link or FA with the minimum latency variation value or not.

## Slide 8: Component Link or FA Selection/Creation
Assume there are following component links within one composite link.
  Component link1: latency = 5ms, latency variation = 15 us
  Component link2: latency = 10ms, latency variation = 6 us
  Component link3: latency = 20ms, latency variation = 3 us
  Component link4: latency = 30ms, latency variation = 1 us
Assume there are following SLA Parameters for component link selection. Only Component link2 could be qualified.
  I bit = TRUE
  V bit = FALSE
  Maximum Acceptable Latency Value= 35 ms
  Maximum Acceptable Latency Variation Value = 10us
Assume there are following SLA Parameters for component link selection. There may be no any qualified component links. Priority may be used for latency and variation.
  I bit = TRUE
  V bit = TRUE
  Maximum Acceptable Latency Value= 35 ms
  Maximum Acceptable Latency Variation Value = 10us
Notes: <number>

## Slide 9: Latency Accumulation and Verification
Latency Accumulation Object
  It is carried in Path/Resv message in order to accumulate the latency of each links and nodes along the path which is across multi-domain.
  When the source node desires to accumulate (i.e., sum) the total latency of one end-to-end LSP, the "Latency Accumulating desired“ flag should be set in the LSP_ATTRIBUTES object of Path/Resv .
Latency Accumulation sub-TLV
Latency Accumulation Object
Non- linearly

## Slide 10: Latency Accumulation and Verification
Required Latency Object
  It is carried in the LSP_ATTRIBUTES object of Path/Resv message.
  If the source node makes the intermediate node have the capability to verify the accumulated latency, the "Latency Verifying desired" flag should be set in the LSP_ATTRIBUTES object of Path/Resv.
  Intermediate nodes could reject the Path or Resv if the accumulated latency exceeds required latency value in this object.

## Slide 11: Next steps
Refine the document according to the feedback of meeting and mailing list.