## Slide 1: MPTCP Enhancements to Improve Applicability to Wireless Access Networks draft_hampel_mptcp_applicability_wireless_networks_00 Georg Hampel, Thierry Klein – Bell Labs + Discussions on ML

## Slide 2
Topics
MPTCP + Wireless Access Networks
2. Low-complexity MPTCP host
3. Signaling & policy enhancements
4. Transparent proxy
5. Summary

## Slide 3
MPTCP + Wireless Access Networks
“What do we gain when using MPTCP in wireless access networks”

## Slide 4
MPTCP: Goals & Constraints (RFC 6182)
Prerequisite:
Availability of multiple paths
Goal
Improve throughput
- resource pooling (“not worse than best path”)
- load balancing
Increase resilience
  - segments can be (re-) send over every path
Constraints
App compatibility: TCP-like, transparent
Nwk compatibility: middle-box compliance
Compatibility with other users: fairness
Security
WLAN
3G/4G
Mobile
Server
How well does this go with wireless?

## Slide 5
MPTCP + Wireless Access Networks: Typical Environment
Datarate
3G
WiFi
2.5G/3G/4G - Macrocellular – Outdoor deployment
Outdoors: Optimized for coverage
Indoors: Wall penetration  low rate
Access: Mostly single-subscribership
WiFi - Hotspot, in home/company – Indoor deployment
Indoors: Optimized for rate
Outdoors: Wall penetration  effectively no coverage
Access: Closed user group
One
outdoor
network
One
indoor
network
Little gain from resource pooling
WiFi

## Slide 6
MPTCP Applied to Wireless Access Networks: TP Simulations
Opportunistic Mobility with Multipath TCP
Costin Raiciu, Dragos Niculescu, Marcelo Bagnulo, Mark Handley
TP Gain: Multipath over Path-select: 10 – 15%
Assumptions:
100% Wifi coverage
Open user group
Multipath
Path-select
Small gains even under optimistic assumptions

## Slide 7
MPTCP Applied to Wireless Access Networks: Power consumption
Opportunistic Mobility with Multipath TCP
Costin Raiciu, Dragos Niculescu, Marcelo Bagnulo, MarkHandley
WIFI = 5.8 Mb/J
3G = 0.8 Mb/J
Outdoors: 3G only option. Indoors: 3G too inefficient.

## Slide 8
Small gain from resource pooling
Increased delay
Always maximum delay given by slowest path
Head of line blocking due to periodic outage on weak paths
High resource usage
Large receiver buffer
Processing & air-interface overhead due to DSS options
Higher battery & spectrum usage due to multiple radios
No solution for incremental deployment  Transparent Proxy
MPTCP + Wireless Access Networks: Issues
“Just pick the best path!”
Throughput aggregation: High cost – little gain

## Slide 9
Local wireless link
Worst link (throughput, fluctuations)
Most expensive link
Information on local wireless link
Measurements: SINR, signal strength
Cost per MB
Use this information to:
Select your own interface
Communicate to peer
Path Selective Operation: How to Pick the Best Path?
Local link information promises to find best path

## Slide 10
Value: Seamless session migration across access networks
Throughput: “Not worse than best path”
Resilience: Same as MP
Load balancing: Same as MP
Application-, middlebox-, fairness-, security compliance: Same as MP
 Meets the goals & constraints of RFC 6182
Cost:  MIN
Lower complexity
Smaller buffer space ( conventional TCP)
Reduced air-interface/battery usage
Reduced processing/air-interface overhead
MPTCP: Enabler rather than performance differentiator
Path-Selective Operation = “Just-pick-the-best-path”: Value & Costs
Low complex host
Signaling optimization
One radio at a time

## Slide 11
Low Complexity Realization
“How cheap can we make path-selective operation”

## Slide 12
 Performance impact seems acceptable
Low Complexity MPTCP Host: Principal Concept
Use only one flow- & congestion engine
Between path-reselection windows  Fine
During path-reselection window:
  Seamless since multiple subflows are up
  Engine needs to adapt to new channel
  Retransmissions on old path or cross flow?
Performance impact
Same as for: Mobile IP family, 3GPP, HIP, SHIM6, etc.
Full-fledged MPTCP host: Needs to adapt to new channel conditions

## Slide 13
Internal interface
MPTCP
SFL Flow/Cong
MPTCP Module: Flexible realization in- or outside kernel
Low-Complex MPTCP Host: Protocol stack
MPTCP
Connection Flow/Cong
Conventional TCP
Connection Flow/Cong
MPTCP full-fledged
(multi engine)
MPTCP low-complex
(single engine)
MPTCP
SFL Flow/Cong
SFL Map/Sgnl
SFL Map/Sgnl
MPTCP Module
Conventional TCP segment
Conventional TCP segment
Conventional TCP segment
Stream socket
Stream socket

## Slide 14
Low-Complex MPTCP Host: Signaling Plane
TCP
Engine
MPTCP
Module
SYN
SYN + MP_CAP
SYN/ACK
SYN/ACK + MP_CAP
ACK
ACK + MP_CAP
SYN + MP_JOIN
SYN/ACK + MP_JOIN
ACK + MP_JOIN
FIN
FIN + Data FIN on DSS
FIN
Packet + DSS, etc
Packet
Establishment of connection & 1st subflow
Establishment of add subflows
MPTCP-specific
signaling
Termination of add subflows
Termination of connection
Signaling compliant with MPTCP protocol
+ ACK

## Slide 15
Low-Complex MPTCP Sender - Data Plane
SN_tcp
AN_tcp
Rewrite segment:
SN_tcp  SN_i
AN_tcp  AN_i
IPsrc_tcp  IPloc_i
IPdst_tcp  IPrem_i
Rewrite segment:
SN_tcp  SN_i
AN_tcp  last AN_i
IPsrc_tcp  IPloc_i
IPrem_tcp  IPrem_i
Create ACK:
SN_tcp  last SN_k
AN_tcp  AN_k
IPsrc_tcp  IPloc_k
IPdst_tcp  IPrem_k
 DSN_loc  SFL i  SFL SN_i
 DSN_rem  SFL k  SFL AN_k
SFL i
SFL i
SFL k
TCP Engine
MPTCP Module
 Processing high if both senders active and not in synch
If i=k
Senders are in synch
Both use the same path
If i!=k
Senders are not in synch
During path re-selection or
if remote sender does multipath
Packet Splitting !

## Slide 16
Low-Complex MPTCP Receiver - Data Plane
SN_tcp Incoming
AN_tcp segment
TCP Engine
MPTCP Module
Rewrite segment:
SN_i  SN_tcp
AN_i  AN_tcp
IPsrc_i  IPloc_tcp
IPdst_i  IPrem_tcp
IPsrc, PRTsrc
IPdst, PRTdst
SFL SN_i  DSN_rem = SN_tcp
SFL AN_i  DSN_loc = AN_tcp
SFL i
Connection-level buffering + reordering: Done by TCP Engine
Multipath-compliant
Large buffer if remote sender does multipath
Subflow-level buffering: Only if mapping unknown
Adds unnecessary complexity! To be avoided!
Availability of mapping crucial for low-complexity !

## Slide 17
DL Multipath
UL Path-Select
DL & UL
Path-Select
Full-fledged
Full-fledged
Low-complex
Accommodate frequent packet split
Accommodate large TCP buffer
Low-complex
Assert peer does path-select
Assert same path is used
Interoperability: Full-Fledged Host  Low-Complex Host

## Slide 18
Low-Complex MPTCP Implementation: Linux 2.26.38 – Ubuntu 11.xx
App
MPTCP Module
TCP
RAW
Netlink
Netfilter
IP
Queue
Filter functions:
Pc, IPsrc, IPdst, PRTsrc, PRTdst
Flags: SYN, ACK,…
Target:
ACCEPT, DROP, QUEUE
IP Tab
mangle
ACCEPT/DROP
cmd
filter
functions
own
packets
User space
Kernel space
filtered packets
Sequential processing
No buffering or reordering possible in user space!
mangled
packets
input/output
packets

## Slide 19
Signaling:
Temporary Fallback mode
No bulk-transfer optimization
Path-selection conflict resolution policy
New MP_PRIO
Trials:
Interoperability with MPTCP full-fledged
(Both hosts path-selective)
(Multipath peer)
LTE/3G vs. WiFi
Low-Complex MPTCP Implementation: Signaling + Trials

## Slide 20
Interface Availability Signaling
“How to tell the server that my interface is down”

## Slide 21
Use case
Mobile client  central server
Client must inform server about its interface availability
Problem with (old) MP_PRIO
Path- rather than interface-specific
Option must be sent on path it refers to
 No way to signal “interface is down” !
Proposal
Provide explicit interface-availability signaling
ML discussion: Add ADDR-ID to MP_PRIO
 Issue addressed in draft-ietf-mptcp-multiaddressed-04
New Signaling: Client Announces Interface Availability to Server
WLAN
3G/4G
Mobile
Server

## Slide 22
Path-Selection Conflict Resolution
“I want paths 1 & 2, you want 3 & 4”

## Slide 23
Policy Required: Conflict Resolution for Path Selection
Question: Why set up a path in backup mode?
Reason: Enjoy resilience  Avoid path cost
Proposed policies:
Differentiate between Paths and Interfaces
Local Interface is the main “cost” factor
1) Peers mutually respect local interface selection
 No conflict!
Host tries to accommodate peer’s path selection
 If no path left, pick one!
Host A
Host B
A wants only these paths.
B wants only these paths.
 Serves multipath- and path-selective operation
Host A
Host B
A wants only this path.
B wants only this path.

## Slide 24
DSS Issues
“How to avoid unnecessary cost”

## Slide 25
Signaling Proposal: Bulk Transfer “Optimization”  Optional
DSS “optimization” on bulk transfers is a tradeoff
Advantages
Reduces number of DSS
Disadvantages
Requires additional queuing on subflow level
Adds delay on sender side
Proposal:
Make feature optional
Add “Bulk Transfer Optimization”-Flag to MP_CAPABLE
 Flag is vital for low-complex realization

## Slide 26
Feature requirement: “Temporary Fallback” Mode
Use case: Mobile sees only one (dominant) path
DSS: Adds overhead, no value
Propose: “Temporary Fallback”
If only one path active, MPTCP becomes as low-cost as TCP  No DSS!
Resume multipath operation when needed
Problems:
How to do the signaling?
How to deal with payload modifying middle boxes?
Proposals   
 Necessary for wireless MPTCP

## Slide 27
Problem with Present Fallback Mode
draft-ietf-mptcp-multiaddressed-04.txt: Section 3.5
“…When a connection is in fallback mode, only one subflow can send data at a time. …However, subflows can be opened and closed as necessary, as long as a single one is active at any point.”
ML discussions: This does not seem to work!

## Slide 28
Proposal: Temporary Fallback + Return --- NO CHECKSUMS
SFL1
DSN = X, SSN = Y
DSS_infinity
SSN = Z, DSN = X
DSN = X+100, SSN = Y+100
DSN = X+400, SSN = A
SSN = B  DSN=X+400
DSS
Temporary Fallback: DSS + infinity setting
Return to Multipath: DSS on any path
Since no payload rewriting, DSN is always absolute reference
SFL2
DSS
DSN = X+200, SSN = Y+200
DSN = X+300, SSN = Y+300
SSN = Z+100, DSN = X+100
SSN = Z+200, DSN = X+200
SSN = Z+300, DSN = X+300
…
…

## Slide 29
Retroactive DSS
DSN= X+400
SSN = 400
Range = 0
Checksum = CSi
SFL1
DSS_infinity
Verify  CSi = CS’i
If match  return to MP
(via DSS)
Otherwise  terminal FB
(via MP_FAIL)
Proposal: Temporary Fallback + Return –-- WITH CHECKSUMS
CS1
+ CS2
+ CS3
+ CS4
CS’1
+ CS’2
+ CS’3
+ CS’4
Catches payload rewriting
Return to MP must occur on present subflow
Procedure must be done “reliably” and in both flow directions
DSN = X, SSN = Y
DSN = X+100, SSN = Y+100
DSN = X+200, SSN = Y+200
DSN = X+300, SSN = Y+300
SSN = Z, DSN = X
SSN = Z+100, DSN = X+100
SSN = Z+200, DSN = X+200
SSN = Z+300, DSN = X+300
DSN = X+400, SSN = A

## Slide 30
Transparent Proxy

## Slide 31
Purpose: Incremental Deployment
Generic proxy: Flexible
Can reside anywhere
Needs signaling to authenticate host
Needs signaling on how to route packets
Transparent proxy: Simple
Resides on central router of initial path
Implicitly authenticated via network access
Derives route from packet inspection
Relevant use case:
Transparent proxy on macro-cellular network
Transparent MPTCP Proxy
LTE
WLAN
MPTCP
Terminal
Server
MPTCP
Transparent
Proxy

## Slide 32
Proposal: “JOIN” Flag + “NEW_TARGET” Flag on ADD_ADDR
MPTCP
TCP
ADD_ADDR
(IP proxy)
MP_JOIN
REMOVE_ADDR
(IP server)
RST
MPTCP
TCP
MP_JOIN
MP_JOIN
MN-LTE
MN-WiFi
Server
Proxy
MPTCP
TCP
ADD_ADDR
(IP proxy)
New Target
MP_JOIN
MP_JOIN
MN-LTE
MN-Wifi
Server
Proxy
Problem: ADD_ADDR is overloaded: Add Address + Join Address
New NEW_TARGET flag: “Use this address for future subflows”

## Slide 33
Summary

## Slide 34
Summary: Proposed Signaling, Policies, Features
Propose: Path-selection conflict resolution policy
Propose: Make bulk-transfer “optimization” optional
Add BULK_TRANSFER_OPTIMIZATION flag to MP_CAPABLE
Propose: Feature for temporary fallback & return to MP
With payload rewriting middle boxes
Without payload rewriting middle boxes
Need clarification of subflow re-selection in Fallback mode
Propose: Support for transparent proxy
Add JOIN flag to ADD_ADDRESS
Add NEW_TARGET flag to ADD_ADDRESS