## Slide 1: Mobile Multicast Sender Support in PMIPv6 Domains with Base Multicast Deployment draft-schmidt-multimob-pmipv6-base-source-00
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Objective of the Draft
Clarify operations of mobile multicast sources at basic deployment of multicast support in PMIPv6 domains – i.e., source mobility in the scenario of draft-ietf-multimob-pmipv6-base-solution
  Demystification: it works
Informational work: No new protocols needed
Pragmatic base approach as for listeners:
  Suboptimal routes are price for simplicity

## Slide 3: Multicast Base Deployment with Mobile Source
+-------------+
| Multicast |
| Receivers |
+-------------+
/ \
+----+ +----+
|LMA1| |LMA2| Multicast Anchor
+----+ +----+
LMAA1 | | LMAA2
| |
\\ //\\
\\ // \\
\\ // \\ Unicast Tunnel
\\ // \\
\\ // \\
\\ // \\
Proxy-CoA1 || || Proxy-CoA2
+----+ +----+
|MAG1| |MAG2| MLD Proxy
+----+ +----+
| | |
MN-HNP1 | | MN-HNP2 | MN-HNP3
MN1 MN2 MN3
Multicast Senders & Receivers
DR or MLD Proxy
MLD Proxy forwards locally and per Uplink

## Slide 4: Efficiency Issues
Routing is optimal for receivers at the sender’s MAG that belong to the same LMA, and for the fixed Internet
Routing detours via LMAs, whenever
  Mobile listener is attached to another MAG
  Mobile listener is associated with a different LMA
No way to suppress the forwarding uplink to LMA
Admission control/rate limiting may be desirable to prevent flooding LMAs

## Slide 5: Summary & Outcome
This draft explains source mobility in the base scenario
Traffic flows/aggregation may be optimal, but need not be
Draft extends minimal solution to senders
  Does not exhaust the issues of source mobility
Question to WG:
Make this a quick informational source
or Extend to optimized routing solution?

## Slide 6
Questions?