## Slide 1: PMIPv6 multicasting support using native infrastructure draft-sijeon-multimob-direct-routing-pmip6-01.txt
Seil Jeon and Younghan Kim
81st IETF, July 2011, Quebec City, Canada

## Slide 2: Definition
Two kinds of terms (direct routing and local routing) confused so we define which is direct routing and local routing for PMIPv6 multicasting in our draft
Direct Routing
  Multicast data is transmitted to a MN using native multicasting infrastructure within operator’s network
Local Routing (Local Content Delivery)
  Content source is directly connected to a MAG
  There’s no need of multicast routing protocol to retrieve multicast data
  MLD proxy function is needed on a MAG to exchange MLD signaling and multicast data between an MN and source

## Slide 3: Direct/Local Routing
Base solution [RFC6424] introduces tunnel convergence problem in case a MAG receives the same multicast packets from more than one LMA
To remove the issue, direct routing is one of the effective multicast data delivery approaches
Local multicast data delivery mechanism is needed for ISPs having their own local contents

## Slide 4: Direct Routing Solution
The key idea is using native multicast infrastructure directly. The idea can be implemented as two cases
  A “MLD proxy” or “MLD + MR” can be placed on a MAG
Multicast data can be retrieved from a variety of content sources

## Slide 5: Applicability
If a multicast listener is in a visited network, the direct routing can be applied on the condition that there are some multicast peering entities in the visited network (i.e., CDN, inter-domain multicast routing protocol like BGMP [RFC3913] or MBGP [RFC4765])

## Slide 6: Comparison
PMIPv6 Extension vs. Direct Routing
 | PMIPv6 Extension | Direct Routing
Multicast function on a MAG | MR on a MAG | MR function can be integrated in a MAG or separated from a MAG
Multicast Routing Protocol | PIM-SM | Any
Interface between LMA and MR | GRE | Any Tunnel
Complexity or Burden in a MAG | Complex and Heavy | Simple and Lightweight (when a MR is separated from a MAG)
Efficiency in Deployment | All MR functions are on a MAG | MLD Proxy on a MAG (when a MR is separated from a MAG)

## Slide 7: Q & A