## Slide 1: Multicast Tree Mobility Anchor (MTMA)
81th IETF, Quebec
MTMA
Juan Carlos Zúñiga, Akbar Rahman
InterDigital
Luis M. Contreras, Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Ignacio Soto
Universidad Politécnica de Madrid (UPM)
MULTIMOB WG, July 2011

## Slide 2: Multicast Tree Mobility Anchor (1/2)
https://datatracker.ietf.org/doc/draft-zuniga-multimob-smspmip/
Basic concept discussed since IETF 76
Scope of Changes:
  Definitions and terminology updated
    Multicast LMA -> Multicast Tree Mobility Anchor
  New considerations added in section 4
  Overhead analysis added in Appendix A
  Added details about reuse of PMIP features such as tunnel establishment, security and heartbeat
81th IETF, Quebec

## Slide 3: Multicast Tree Mobility Anchor (2/2)
Features
  Not all LMAs need to support multicast capability and connectivity
    Reduces total resources and states at LMAs
    Reduces tunnel convergence issue at the MAG
    Minimizes the replication of multicast traffic when MNs with different LMAs join the same multicast group
  Simplifies the multicast tree topology
    Allows a PMIPv6 domain to closely follow a simple multicast tree topology for Proxy MLD forwarding
  Allows the implementation of a single MLD proxy instance per MAG to support the multicast service
    Reduces the complexity of the MAG
  Permits different PMIPv6 deployment scenarios
    Deployment strategies can be tailored for expected traffic scenarios
81th IETF, Quebec

## Slide 4: Backup Slides
81th IETF, Quebec

## Slide 5
Dedicated M-LMA architecture
Local Routing architecture
Brief description of M-LMA approach
MAGs incorporate MLD proxy functionality
Dedicated infrastructure for multicast service delivery to MNs in PMIPv6 domain
Multicast traffic to MNs tunnelled from Home Network Provider
Brief description of Local Routing approach
MAGs incorporate MLD proxy functionality
Multicast infrastructure should be available in PMIPv6 access provider
Multicast traffic to MNs is natively served from Access Provider

## Slide 6: Major advantages of M-LMA approach
81th IETF, Quebec
Service provision
  M-LMA allows for a total control by the Home Network Provider of the service delivered to the MNs while moving in a PMIPv6 domain, facilitating the billing, the QoS provision, etc.
Service definition
  M-LMA does not need multicast addressing coordination per content between both providers, e.g. to avoid address overlapping. Hence, it makes the multicast service provision independent from one provider to the other
Service deployment
  M-LMA facilitates the multicast service deployment because the node providing multicast service (e.g. M-LMA) is well identified. Hence, there is no need to do customization of multicast router definition on every PMIPv6 domain available for the MNs
Others
  Most of the existing PMIPv6 features (security, load balance, heartbeat, etc) can be directly re-used

## Slide 7: Minor drawbacks of M-LMA approach (as per draft-sijeon-multimob-direct-routing-pmip6-00)
81th IETF, Quebec
LMA signaling process overload
  In fact, both solutions have similar multicast signaling processing requirements. M-LMA only requires additional tunnel establishment, which is negligible due to the semi-permanent nature of the tunnels.
  Even if tunnels are dynamically created, the same tunnel is used for all the multicast traffic, for all the MNs in the PMIPv6 domain
Overhead
  The tunneling process in M-LMA approach imposes an overhead of 40 bytes due to the tunnel heading. Nevertheless, the typical multicast packet length is large in nature and the average overhead is minimal
      Case study: MPEG-2 TS over IP video transmission
      video packet length = 7*188 = 1316 bytes
      RTP header = 12 bytes
      UDP header = 8 bytes
      IPv6 header = 40 bytes
      Total length = 1376 bytes
      Tunnel overhead= 40 / (40 + 1376) = 2,8%

## Slide 8: Comparison table
Main feature
Allows home billing
Requires MAG upgrade
Avoids tunnel convergence problem
Allows multicast services from Visited
Allows multicast services from Home
No need for multicast addressing coordination between providers