## Slide 1: Tuning the Behavior of IGMP and MLD for Routers in Mobile and Wireless Networks
draft‐ietf‐multimob‐igmp‐mld‐tuning-01
Hitoshi Asaeda
Hui Liu
Qin Wu
81st IETF, July 2011, Quebec City, Canada

## Slide 2: Summary
This document describes the ways of IGMPv3 and MLDv2 protocol optimization for mobility, and aims to become a guideline for query and other timers and values tuning.
Potential tuning values are clarified
  Query Interval
  Query Response Interval
  Last Member Query Timer (LMQT) / Last Listener Query Timer (LLQT)
  Startup Query Interval
  Robustness Variable

## Slide 3: Changes
Document title change
  “Tuning the Behavior of IGMP and MLD for Routers in Mobile and Wireless Networks”
    Explicitly focus on tuning timers and values for routers
Add one use case in introduction section to explain the challenge of using IGMP/MLD in mobile network
Add section 4.6, “Tuning Scenarios for Various Mobile IP Networks”
Refer RFC6224
Editorial changes

## Slide 4: 4.6 Tuning Scenarios for Various Mobile IP Networks
Three deployment scenarios
  IGMP/MLD running directly between host and access router on a wireless network
    routing optimization for Mobile IP and PMIPv6 applies
    Treat it in the same way as it in the wireless network
  IGMP/MLD running between host and home router through a tunnel link
    Shorter [Query Interval] and [Query Response Interval], and larger [Robustness Variable] value at the beginning of the session
      Because message transmission depends on the condition of the tunnel link
    Enlarge the Query periodicity in case of congestion
  IGMP/MLD running between home router and foreign router through a tunnel link (e.g. RFC6224)
    [Query Response Interval] on the home router or local mobility anchor could be set to the smaller value
      Because the number of foreign router is much smaller than usual
    Enlarge the Query periodicity in case of congestion.

## Slide 5: Next Step
We appreciate your review
Expect to issue new version to address the comments during the meeting.
WGLC?
  Intended status: Informational?