## Slide 1: Fast Handover For Multicast in Proxy Mobile IPv6
Dapeng Liu/Min Hui/Hui Deng

## Slide 2: Motivation
The existing solution for PMIPv6 multicast specifies that, only after the bi-directional tunnel is built between n-MAG and LMA using the multicast packet can be continuously delivered to MN.
It inevitably causes the latency and loss of packet during handover process
Proposal: A fast handover mechanism to support multicast for PMIPv6

## Slide 3: PMIP multicast fast handover Solution Overview
LMA
P-MAG
n-MAG
MN
MN
P-MAG and N-MAG establishing
bi-directional tunnel to forward
multicast traffic
Extend HI (handover Initiate) message to carry multicast context information

## Slide 4: Handover Procedure
MN
P-MAG
n-MAG
LMA
(1) HO Initiate
(MN ID, n-MAG ID)
(2) HI
(MN ID, Multicast State)
(3) HAck
(4) HI/HAck
(7) Multicast Data
(8) PBU-M
(9) PBA
(10)Multicast Data
(11)HI/HAck
(5)
(6) Handover

## Slide 5: Extension of HI message
A new flag (M) is included in the HI Mobility Header message with
multicast extension. The rest of the message format remains the same
as defined in [3].
When (M) flag is specified in HI Mobility Header message, the
mobility options field needs to be extended to include the multicast
addresses.

## Slide 6: Discussion
What is the next step?