## Slide 1: Issues in Tunnel Convergence Solutions
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Two Types of Tunnelling Problems
Convergence
  Multiple tunnels terminate at MAG, possibly transporting duplicate traffic
  Inherent to the PMIP base solution
Avalanche
  Tunnel head serves many MAGs causing a high replication load of identical traffic
  Inherent to the M-Head (M-LMA) proposal

## Slide 3: Further Objectives
Enhance Service Availability
  Extend access to multicast channels
Reduce Service Cost
  Optimize access / routing to reduce network load
Remain transparent with respect to PMIP evolution
  In particular: Cross-domain access

## Slide 4: Use Cases
Case 1:
  User wants to have access to home subscription channels while moving to a visited network
Case 2:
  User may want (to pay extra fees) to access local content depending on location (e.g., pay-TV in hotel)
Case 3:
  If content can be accessed from more than one location, MAG could select the best path based on routing cost

## Slide 5: Current Solutions / Proposals
Base Solution:
  Covers use case 1, tunnel convergence problem
Direct Routing:
  Covers use case 2, optimized – but requires local mcast routing
M-Head/M-LMA:
  Covers use case 1, avalanche problem
All-PIM Domain:
  Unclear: depends on non-PMIP unicast routing at MAGs, most likely equivalent to direct routing

## Slide 6: Path to Solution & Problems
Objective from Use Cases:
Combine base solution (home subscription) with local service access
Problems to solve:
  Multicast routing intelligence at MAGs
    How to access which group?
  Make handover smooth & policy-compliant
    Handle mixed access seamless without access violations