## Slide 1: Multran Requirements draft-jaclee-behave-v4v6-mcast-ps-02
Mohamed Boucadair (mohamed.boucadair@orange-ftgroup.com)
Christian Jacquenet (christian.jacquenet@orange-ftgroup.com)
Dean Cheng (chengd@huawei.com)
Yiu Lee (yiu_lee@cable.comcast.com)
IETF77, Anaheim
Christian Jacquenet, France Telecom
Mohamed Boucadair, France Telecom
Jacni Qin, ZTE
Tina Tsou, FutureWei Technologies
Yiu Lee, Comcast
IETF 81, Quebec City

## Slide 2: Requirements
R1: Transition mechanisms to access content must be transparent to IPv4 and IPv6 receivers.
R2: Re-use existing multicast protocols (IGMP, MLD, PIM).
R3. Require a standardized address format for interworking IPv4 and IPv6 multicast family addresses.
R4: Require IWF for control protocols (e.g. IGMP <-> MLDv2).
R5. Support both ASM and SSM.
R6: Current multicast operation procedures should be preserved.
R7: Content integrity must be preserved.
R8: Transition mechanism must not degrade QoS and customer’s QoE.

## Slide 3: Requirements
R9: Content should be sent only once in the network to preserve bandwidth.
R10: S4 -> R6 and S4 -> N6 -> R4 scenarios have higher priority to be addressed.
R11: If double-translation is used (ie. 4-6-4 or 6-4-6), the 2nd transition should translate the input multicast group address back to the original multicast group address.

## Slide 4: Questions?