## Slide 1: IPv4-IPv6 Multicast Scenarios
M. Boucadair, C. Jacquenet X.Deng

## Slide 2: Context
The reality of global IPv4 address depletion challenges the delivery of multicast-based services e.g.,
  Access infrastructures that assume a service-agnostic, publicly-addressed single PVC to convey all kinds of traffic including,
    Multicast service-related unicast traffic (e.g. EPG consultation)
    Integrated unicast traffic (e.g. Internet Gaming, Surfing, through TV Set box)
  Access to IPv4 formatted contents that is multicast to customers who are not provisioned with a dedicated global IPv4 address anymore (e.g. user management, traffic engineering)
Migration towards IPv6 cannot be done overnight
  Also true for multicast-based services

## Slide 3: Dual Stack?
Supposed to be the most straightforward deployment model where,
  Both multicast networks and sources (for a given content) are dual-stack
  Receivers can then select the contents depending on their capabilities
But dual stack sources are NOT always available
  Depends on the content provider’s strategy
Not compatible with unicast transition cases
  E.g., DS-Lite deployment mode, NAT64

## Slide 4: Main Characteristics of DS
Pros | Limitations
Simple | CAPEX (e.g., bandwidth cost)
 | Requires coordination between the content and the network providers
 | Not compatible with unicast transition cases, e.g. despite DS-formatted content, extensions are still required to deliver the content to IPv4-only receivers when DS-Lite is deployed
    * There will be a mix of “receivers”, “sources”, “networks” running in different address families and probably a mismatch of the address family.

## Slide 5: “Mono-Stack”
Definition: the delivery infrastructure is NOT wholly dual-stack enabled when,
  The source is reachable only with one single address family or,
  The delivery network is IPv4-only enabled, IPv6-only enabled, or a hybrid of partially IPv4-enabled and partially IPv6-enabled.

## Slide 6: Use cases of “Mono-Stack”
Use Cases | *Network Capabilities | Source | Receiver | Categories
1 | IPv4 | IPv4 | IPv6 | Translation
2 |  | IPv6 | IPv4 | 
3 |  | IPv6 | IPv6 | Traversal
4 | IPv6 | IPv4 | IPv6 | Translation
5 |  | IPv6 | IPv4 | 
6 |  | IPv4 | IPv4 | Traversal
Hybrid | IPv4, IPv6 | IPv4, IPv6 | IPv4, IPv6 | Hybrid
 |  | IPv4, IPv6 | IPv4, IPv6 | 
    * There are 3 variables, hold one (network) so as to simplify the discussions
    * The “native” portion is not taken into account since there is no extra function needed, e.g. “DS Source + IPv6 Network + DS Receiver” is simplified as “IPv4 Source + IPv6 Network + IPv4 Receiver” (Use Case #6)

## Slide 7: IPv4 Delivery Network
IPv4 Network
S4
R4
DR
QR
S6
R6
S6 = v6 Source
R6 = v6 Receiver
S4 = v4 Source
R4 = v4 Receiver
DR = Designated Router
QR = IGMP/MLD Querier
Use cases 1, 2, 3

## Slide 8: IPv6 Delivery Network
IPv6 Network
S6
R6
DR
QR
S4
R4
S6 = v6 Source
R6 = v6 Receiver
S4 = v4 Source
R4 = v4 Receiver
DR = Designated Router
QR = IGMP/MLD Querier
Use cases 4, 5, 6

## Slide 9: Hybrid Delivery Network
IPv4 Network
IPv6 Network
S4
R4
MR
S6
R6
S6 = v6 Source
R6 = v6 Receiver
S4 = v4 Source
R4 = v4 Receiver
MR = Multicast Router, could be border router connecting IPv4
and IPv6 network, or DR connecting the source, or QR
connecting the receiver
Hybrid cases
MR
MR
…
…

## Slide 10: Translation Cases
Use cases and detailed scenarios according to different locations of the “multicast translator” (mXlate),
  IPv4 Source --> IPv6 Receiver, e.g.:
  IPv6 Source --> IPv4 Receiver
R6
DR
S4
R6
IPv6 Distribution
Tree
R6
QR
S4
IPv4 Distribution
Tree
IPv6 Distribution
Tree
IPv4 Distribution
Tree
MR
R6
R6
S4
Scenario 1:
Scenario 2:
Scenario 3:

## Slide 11: Traversal Cases
Use cases and possible forwarding mechanisms
  Deliver IPv4 contents to IPv4 receiver over IPv6 network (4-6-4, e.g., DS-Lite environment)
    Encapsulation
    Double-Translation
  6-4-6 scenario?