## Slide 1: NEA Working Group IETF meeting
July 27, 2011

## Slide 2: Note Well
Any submission to the IETF intended by the Contributor for publication as all or part of an IETF Internet-Draft or RFC and any statement made within the context of an IETF activity is considered an "IETF Contribution". Such statements include oral statements in IETF sessions, as well as written and electronic communications made at any time or place, which are addressed to:
The IETF plenary session
The IESG, or any member thereof on behalf of the IESG
Any IETF mailing list, including the IETF list itself, any working group or design team list, or any other list functioning under IETF auspices
Any IETF working group or portion thereof
The IAB or any member thereof on behalf of the IAB
The RFC Editor or the Internet-Drafts function
All IETF Contributions are subject to the rules of RFC 5378 and RFC 3979 (updated by RFC 4879).
Statements made outside of an IETF session, mailing list or other function, that are clearly not intended to be input to an IETF activity, group or function, are not IETF Contributions in the context of this notice.
Please consult RFC 5378 and RFC 3979 for details.
A participant in any IETF activity is deemed to accept all IETF rules of process, as documented in Best Current Practices RFCs and IESG Statements.
A participant in any IETF activity acknowledges that written, audio and video records of meetings may be made and may be available to the public.

## Slide 3: Agenda Review
1300 Administrivia
Jabber & Minute scribes
Agenda bashing
1305 WG Status
1310 NEA Reference Model
1315 Discuss and Resolve Open PT-TLS Comments
http://www.ietf.org/internet-drafts/draft-ietf-nea-pt-tls-00.txt
1400 Discuss and Resolve EAP vs. TLVs for L2 PT
http://www.ietf.org/internet-drafts/draft-cam-winget-eap-tlv-03.txt
http://www.ietf.org/internet-drafts/draft-hanna-nea-pt-eap-01.txt
1500 Adjourn

## Slide 4: WG Status
PT-TLS WG I-D published
No consensus on EAP transport
  Architectural differences on EAP method/TLV approaches discussed on mailing list

## Slide 5: NEA Reference Model

## Slide 6
NEA Reference Model from RFC 5209
Posture
Collectors
Posture
Validators
Posture
Transport
Server
Posture Attribute (PA) protocol
Posture Broker (PB) protocol
NEA Client
NEA Server
Posture Transport (PT) protocols
Posture
Transport
Client
Posture
Broker
Client
Posture
Broker
Server

## Slide 7: PA-TNC Within PB-TNC Within PT
PT
PB-TNC Header
PB-TNC Message (Type=PB-Batch-Type, Batch-Type=CDATA)
PB-TNC Message (Type=PB-PA, PA Vendor ID=0, PA Subtype= OS)
PA-TNC Message
PA-TNC Attribute (Type=Product Info, Product ID=Windows XP)
PA-TNC Attribute (Type=Numeric Version, Major=5, Minor=3, ...)

## Slide 8: PT-TLS Evaluation

## Slide 9: Agenda
Summarize PT-TLS
Creation of -00 I-D
  Integration of PT-TLS and PT-TCP
  Use of SASL for client authentication
  Reduced mention of TCG
Questions
Next Steps

## Slide 10: PT-TLS Message Format
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Message Type Vendor ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Identifier |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Value (e.g. PB-TNC Batch) . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Format matches PB-TNC Message header (plus Message Identifier)

## Slide 11: Three Phases of PT-TLS
TLS Handshake
  Unmodified
Pre-Negotiation
  Version negotiation
  Optional Entity authentication
Data Transport
  NEA assessments

## Slide 12: SASL Entity Authentication
Five SASL oriented messages
  Request SASL Mechanisms
  SASL Mechanisms
  SASL Mechanism Selection
  SASL Authentication Data
  SASL Result
MUST support SASL mechanisms
  PLAIN and EXTERNAL
One mechanism at a time (multiple allowed)

## Slide 13: PT-TLS SASL Message Flow
PT-TLS
Initiator
PT-TLS
Responder
Request SASL Mechanisms (Optional)
SASL Mechanisms (Optional)
SASL Mechanism Selection
SASL Mechanism Data
…
SASL Result

## Slide 14: Either Side Can Start
Client goes first, can send:
  Request SASL Mechanisms to discover list
  SASL Mechanism Selection to pick one proactively
Server goes first, can send:
  SASL Mechanisms proactively
Synchronization
  Client ignores unrequested SASL Mechanisms unless to trigger selection

## Slide 15
Request SASL Mechanisms Payload
Empty (zero length) value field
Optionally sent by TLS Client (unauthenticated party)
TLV requests list of SASL mechanisms offered by recipient
Can be requested at any time

## Slide 16: SASL Mechanisms Payload
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsvd| Mech-Len| Mechanism-Name (1-20 bytes) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsvd| Mech-Len| Mechanism-Name (1-20 bytes) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ . . . . . . . . ~
Sent in response to Request SASL Mechanisms
  Server can proactively send mechanism list
  Client ignore unexpected mechanism lists
Includes prioritized list of SASL mechanisms offered

## Slide 17: SASL Mechanism Selection Payload
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsvd| Mech-Len| Mechanism-Name (1-20 bytes) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Optional Initial Mechanism Response |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Sent in response to SASL Mechanisms
  TLS Client can proactively select mechanism
TLS client selects mechanism to use

## Slide 18: SASL Mechanism Data Payload
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ SASL Mechanism Message (Variable Length) ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Sent by SASL mechanisms (both sides)
Not interpreted by PT-TLS layer
Not sent after SASL Mechanism Result unless additional mechanism to be used

## Slide 19: SASL Result Payload
Result of SASL exchange
  Success, Abort, Mechanism Failure, Not Authorized
Optional additional result data
Completes SASL mechanism exchange
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Result Code | Optional Result Data |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . . . . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 20: Questions
SASL TLVs are mandatory to implement, optional to use
  OK?
PLAIN and External SASL Mechanisms are mandatory to implement
  Do we need any other mechanisms?

## Slide 21: PT-TLS Message Format
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Message Type Vendor ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Identifier |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message Value (e.g. PB-TNC Batch) . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Format matches PB-TNC Message header (plus Message Identifier)

## Slide 22: Next Steps
Publish -01 I-D based on feedback
Request WG last call for comments
Final PT-TLS discussion at IETF 82

## Slide 23: L2 PT Evaluation

## Slide 24: L2 PT Comparison
 | PT-EAP | NEA-TLV
Encapsulation | EAP method inside EAP tunnel | TLV inside EAP tunnel
Proxy | Supported, but needs protection | Not defined
Implementations | 9 | 1
Architecture | Non-authenticating EAP method | Does not use EAP method
Authentication, NEA sequencing | Serial | Serial and Parallel
Key export | Optional, but value unclear | Not supported
Standards | TCG | New I-D

## Slide 25: Consensus Check Question
Prefer PT-EAP approach ?
Prefer NEA-TLV approach?
Neither

## Slide 26: Milestones
Jun 2011 Publish -00 NEA WG PT-TLS I-D
Jul 2011 Resolve issues with PT proposals
Aug 2011 Publish -01 NEA WG PT-TLS I-D
Publish -00 NEA WG EAP-based PT
Sept 2011 WGLC on NEA WG PT I-Ds
Nov 2011 Resolve issues from WG LC at IETF 82
Dec 2011 Send to IESG for IETF Last Call

## Slide 27: Adjourn