## Slide 1
IP Traffic Offload Option for Proxy Mobile IPv6
<number>
<number>
<number>
draft-gundavelli-netext-pmipv6-sipto-option-01.txt
IETF 80: NETEXT Working Group – Access Network Information Option for Proxy Mobile IPv6
Contributors:
Sri Gundavelli (Editor, Cisco), Xingyue Zhou (ZTE),
Jouni Korhonen (NSN), Gaetan F, Rajeev Koodli (Cisco)
Notes: <number>
<number>

## Slide 2: Motivation
In Proxy Mobile IPv6, the IPv4 home address delivered to a mobile node is anchored on the local mobility anchor in the home network.
All the IP traffic from the mobile node using this IPv4 address, is always reverse tunneled by the mobile access gateway in the access network to the home network.
With the exponential growth in the mobile data traffic, mobile operators are exploring new ways to offload some of the IP traffic flows at the nearest access edge where ever there is an internet peering point, as supposed to carrying them all the way back to the home network.
Notes: <number>

## Slide 3: Motivation (Contd..)
Not all IP traffic needs to be routed back to the home network, some of the non-essential IP traffic which does not require IP mobility support can be offloaded at the mobile access gateway in the access network.
This approach provides greater leverage and efficient usage of the mobile packet core with increased overall network capacity and by lowering transport costs.
The local mobility anchor in the home network can potentially deliver the IP flow selectors to the mobile access gateway in the access network, for selecting the IP flows that needs to be offloaded.
Notes: <number>

## Slide 4: IP Traffic Offload Support
The ability to offload “certain” IP flows at the MAG. Or, the inverse capability supporting “Except” offload rule”.
Macro Cell
Access
MAG
LMA
Home Network
802.11 AP
Access Network
Internet
Local Internet Offload Point
Home Routed Traffic
App-2
App-1
N
A
T
802.11 AP
Notes: <number>

## Slide 5: IP Traffic Offload Selector Option
The Offload traffic selector sub-option carried in PMIPv6 signaling includes the parameters used to match packets for offload/upload:
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Type | Length |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |O| RESERVED | TS Format |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | RFC-6088 IPv4 Binary Traffic Selector Option(s) |
  . .
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  The Sub-Type identifies the Offload Traffic Selector Option
  The “O” Flag identifies the offload/upload direction
  This option can be present in PBU/PBA messages
Notes: <number>
<number>

## Slide 6: Traffic Offload Granularity
The select rules for offload/upload traffic can be scoped at different levels. However, in practical terms only few options make sense and can be supported
Filter | Scope
Destination Prefix | Operator value added services
IP Flow Tuple | src/dst address, src/dest port
Application Granularity | Application identifiers (Dest Port or IP Address)
Access Network Identifiers | 802.11 SSID
APN (PDN Identifier) | With single APN support for WLAN access, not an option for IPv4
{ Except-Offload-All Rule } | The approach of VPN Split Tunneling
Notes: <number>

## Slide 7: IP Traffic Offload Selector for PMIPv6
The IP Traffic offload selector option is exchanged between the MAG and LMA as a mobility option over PMIPv6
The mobility option container will leverage the RFC-6088 option formats, IPv4 binary traffic selector option will identify the flow selectors.
WI-FI
Exchange of Offload Traffic Selectors over PMIPv6 Signaling
Offload Rule
LMA
internet
IP Flows
T
O
F
MAG
N
A
T
Notes: <number>

## Slide 8: Offload Policy Enforcement on MAG
The offload policy is applied on the input interface of the MAG in the access network
The output interface for each IP flow from the mobile node, if its towards internet or home network is based on the policy
Internet
Home
Network
MAG
Interface-1
Offload policy Enforced
on input interfaces
Flow Selector | Input Interface | Output Interface
F1 | VLAN-0 | Tunnel-0
F2 | VLAN-1 | Interface-1
Tunnel-0
Access
Network
Notes: <number>

## Slide 9
Thank You
Notes: <number>