## Slide 1: Proposals to RELOAD for Client Promotion and Peer Demotion
IETF81@Quebec
draft-peng-p2psip-promotion-00
Jin Peng
Lingli Deng
Lifeng Le
Gang Li
Notes: <number>

## Slide 2: Motivation
Reload
  a uniform protocol for both clients and peers,
  only active client promotion is provided
User-owned Clients (UNs)
  collectively make the majority of overlay population and the under-exploited vast resource pool
  individually featured with more restrictive resource limits, considerable capability heterogeneity, and diverse interest groups
Problem
  We want to promote UNs to peers.
    in order to reduce service operator's CAPEX
  But only in a cautions manner.
    for imprudent peer behavior causes undesirable implications in P2P networks

## Slide 3: Problem Statement - Overview
Functionalities:
  Passive promotion instead of active promotion
  passive demotion as well as active demotion
Security Considerations
  Explicit authorization for promoted clients
  Timely revocation for misbehaving peers

## Slide 4: Passive Promotion instead of Active Promotion
Considerations
  Proactive regulations are needed for UE-oriented client promotion for
    A UE may be incapable of serving others
    A UE may be malfunctioning in serving others
    A moderate network size may be preferred to remain efficient overlay routing
  The current join-update method allows for active promotion only
Proposals
  The promoter (e.g. an overloading peer) rather than the UE in question triggers the passive promotion procedure
  The promoted UE is selected and certified by the promoter
Extensions to Reload
  Extensions to Probe and Join messages
  Modified client promotion procedure
Notes: <number>

## Slide 5
Passive Demotion as well as Active Demotion
Considerations
  Active demotion decision from the UE side
    User ceases being a peer if he/she perceives a considerable decrease in user experience
  Passive demotion decision from the overlay side to get rid of unnecessary UE-promoted peers:
    Case 1: Overlay decides to shrink its peer group to maintain a tolerable routing delay;
    Case 2: Admin decides to exclude the peer(s) for unsatisfactory service provision
Proposals
  For active demotions:
    ungraceful/graceful demotion procedure
  For passive demotions:
    Case1: graceful demotion procedure;
    Case2: pushed authorization revocation
Extensions to Reload
  Extensions to Leave method to enable graceful demotion
  Pushed authorization revocation
Notes: <number>

## Slide 6
Separate Authorization & Timely Revocation
Considerations
  Explicit authorization to distinguish a UE’s potential to serve as a peer as well as a client
  Timely revocation to limit the impact of a misbehaving peer
Proposals
  Qualified UE acquires a separate peer certificate to attest its capabilities and willingness to serve as a peer.
  A UE-promoted peer’s certificate is revoked if it fails to deliver expected performance while remaining its client certificate intact.
Extensions to Reload
  Separated client and peer authorization
  Active certificate revocation

## Slide 7: THANK YOU!