## Slide 1: The IEEE 802.22 WRAN Standard and its interface to the White Space Database
Gérald Chouinard
IEEE 802.22 Working Group Vice-chair and lead editor
Program Manager
Rural and Remote Broadband Access
Communications Research Centre, Canada
IETF PAWS Working Group Meeting Québec City 26 July 2011

## Slide 2: IEEE 802 Standards Process
IEEE
802
802.11
WLAN
802.15
WPAN
802.16
WMAN
802.11g
54 Mbit/s
802.11b
11 Mbit/s
…
802.15.1
Bluetooth
802.15.3
High rate
802.11n
100 Mbit/s
…
802.16d
Fixed
802.16e
Mobile
…
802.18
Regulatory
Matters
802.22
WRAN
802.22.1
Enhanced Part 74 protection
802.22.2
Recommended Practice
802.11j
Relay
…
802.15.4
Zigbee
Wi-Fi
Wi-MAX
802.19
802 systems
coexistence
Sensing
Tiger Team
Geolocation
Tiger Team
802.19.1
TVWS
coexistence
Notes: The 802.22 Working Group is developing the WRAN standard. It is one of the many 802 WGs as can be seen. This WG is the first one that considers the sensing on incumbent systems already operatin in the frequency range to be used. Each CPE and base station will sense the spectrum in its surrounding and will report it to the base station so that a network level decision is made on either continuing to operate on the channel or switch channel to avoid interference to an incumbent system.
802.22 already has a Task Group 802.22.1 dealing with the development of a standard for a wireless microphone beacon to protect wireless microphone operation in the TV bands since the power of the microphone themselves suffers too much attenuation and cannot be relied upon for sensing.
A second 802.22 Task Group 802.22.2 will be formed in September to develop the “Recommended Practice” to define the proper Installation and Deployment of IEEE 802.22 WRAN Systems so that interference to incumbent systems is avoided. This extra piece will be needed to convince the broadcasters that actual operation will not be harmful to their operation.

## Slide 3: IEEE 802 Standards
IEEE 802.22
RAN
“Regional Area Network”
30 km
54 - 862 MHz
Multipath absorption Window (Cyclic prefix )
0.25
2.2 μsec
0.8
37 μsec
23, 27, 31 Mbit/s
BW= 6,7,8 MHz
Notes: The IEEE 802.22 Working Group which is developing the WRAN standard is adding anotherr layer to the set of licensed-exempt wireless systems. It will be able to operate in the low-VHF (ch. 2-6), high-VHF (ch. 7-13) and UHF (ch. 14 to 51 and 69 where possible). It will use the standard TV channels, 6, 7 and 8 MHz wide. Each channel can carry some 20 Mbit/s capacity and its modulation (2000 carriers OFDMA) will be robust to long echoes (up to about 25 usec) found on these longer paths.

## Slide 4: IEEE 802.22 WRAN Standard Key features
WRAN: Wireless Regional Area Network
  Aimed at bringing broadband access to hard-to-reach, low population density areas, typical of rural environments and developing countries
Operate in vacant channels in TV broadcast bands to take advantage of better signal propagation at lower frequencies
Operate as license-exempt equipment although the base station (BS) and possibly the customer premise equipment (CPE) have to be professionally installed
Point-to-multipoint network topology
  Base station connected to the Internet through a backhaul
  Base station provides service to up to 512 CPEs (fixed or portable) and controls all their RF characteristics (“master-slave”)
Use cognitive radio capabilities to avoid interference to broadcast incumbents and other WRAN systems
  Access to databases
  RF sensing

## Slide 5: Characteristics of 802.22 WRAN:
30 km
23 km
16 km
QPSK
16-QAM
64-QAM
Max throughput per 6 MHz: DS: 7.8 Mbit/s (net: 3.89 Mbit/s)
US: 768 kbit/s (net: 384 kbit/s)
Max throughput per 6 MHz: 23 Mbit/s (net: 19.44 Mbit/s)
Minimum service availability: location= 50% time= 99.9%
Base station power: 100 W Antenna height: 75 m
User terminal (CPE) power: 4 W antenna height: 10 m
USA: ≤ 4 W max EIRP
Height ≤ 30 m (106 m HAAT)
Canada: ≤ 500 W max EIRP
Height ≤ 500 m HAAT (4 W)
Notes: The service availability is defined as F(50, 90), that is one household over 2 can be reached at the edge of the coverage (unlike 1 over 4 over most of the coverage for WLAN as explained by STORM yesterday) (availability will be much better inside the coverage area) and once connection is feasible, its availability in time will be very high for stable service, i.e., 99.9%). This can be achieved with Customer Premise Equipment (CPE) transmit power of 4 W as specified by the FCC and a base station power of 100 W at 75 m antenna height for the maximum throughtput indicated. In order to re-use a DTV frequency, the base station will need to be located at some 30 km from the edge of the DTV coverage area. This will reduce to 1 km if a first adjacent channel is used. The CPEs can be located at 3 km from the edge of the DTV coverage area for the co-channel case and only 70 m for the first adjacent channel. Since it is considered that the distance between neighbor can be as small as 10 m, CPEs operating on first adjacent channels will not be allowed inside the DTV coverage area.

## Slide 6: Typical CPE installation
Sensing antenna
GPS antenna
TX/RX WRAN Antenna
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: 802.22 database interface model
To comply with the FCC R&O 08-260, the IEEE 802.22 interface to the database will take place entirely between the database service and the BS rather than with its individual CPEs (BS has to find the channel that is common to all its CPEs rather than the CPEs doing it individually (MO&O 10-174: 15.711(e)).

## Slide 8: 802.22 database interface procedure
The BS will initially enlist with the database service as a fixed device. It will also enlist all its associated CPEs with their geographic location, device identification, etc., as obtained at association on a real time basis.
On an ongoing basis, the BS will then query the database (at least once every 24 hours) using the M-DB-AVAILABLE-CHANNEL-REQUEST message so that it can retrieve the channel availability information.
The database service could also send any update relevant to the BS operation through ‘push’ internet technology since the network address of the base station is provided as part of the messages (this will allow better reaction time than the 24 hours minimum access time while keeping the database traffic to a minimum).

## Slide 9: Security of the database interface
SSL will be supported on the link between the database service and the BS to provide transport layer security:
  to allow authentication of the database service provider as well as the WRAN system querying the service
  to avoid the message exchange being altered on the backhaul connection
protocols used for device and database service authentication and for interacting with the database: EAP-TLS or EAP-TTLS
database service primitives are exchanged between the CPE/BS and the database service via Attribute Value Pairs of EAP messaging
formatting of these messages should conform to the authentication service that the database service employs: (e.g., RADIUS/RFC 2865 or DIAMETER/RFC 3588).

## Slide 10: Database service primitives
M-DB-AVAILABLE-REQUEST: Message that allows the BS to verify that it is connected to the database service in order to receive channel availability and maximum allowed EIRP updates.
M-DB-AVAILABLE-CONFIRM: Message that allows the database service to confirm that the BS is connected to the database service.
M-DEVICE-ENLISTMENT-REQUEST: Message that allows the BS to enlist with the database service a device that has joined its WRAN network.
M-DEVICE-ENLISTMENT-CONFIRM: Message that allows the database service to confirm to the BS that the new device has been successfully registered.

## Slide 11: Database service primitives
M-DB-AVAILABLE-CHANNEL-REQUEST: Message by which the BS requests a list of available channels and maximum allowed EIRP per channel from the database service for the specified type of device at the particular location.
M-DB-AVAILABLE-CHANNEL-INDICATION: Message that is used to return to the BS the list of available channels as provided by the database service in the form of channel number, maximum allowed EIRP, and availability schedule.
M-DB-DELIST-REQUEST: Message that allows the BS to request the database service to remove the enlistment of a device that was associated with that base station.
M-DB-DELIST-CONFIRM: Message that is used to inform the BS whether its request to remove the enlistment of a device that was associated with that base station was successfully received and executed by the database service.

## Slide 12: M-DB-AVAILABLE-REQUEST

## Slide 13: M-DB-AVAILABLE-CONFIRM

## Slide 14: M-DEVICE-ENLISTMENT-REQUEST (a)

## Slide 15: M-DEVICE-ENLISTMENT-REQUEST (b)

## Slide 16: M-DEVICE-ENLISTMENT-REQUEST (c)

## Slide 17: M-DEVICE-ENLISTMENT-CONFIRM

## Slide 18: M-DB-AVAILABLE-CHANNEL-REQUEST

## Slide 19: M-DB-AVAILABLE-CHANNEL-INDICATION

## Slide 20: M-DB-DELIST-REQUEST

## Slide 21: M-DB-DELIST-CONFIRM

## Slide 22: References
IEEE Std 802.22-2011TM, Standard for Wireless Regional Area Networks—Part 22: Cognitive Wireless RAN Medium Access Control (MAC) and Physical Layer (PHY) specifications: Policies and procedures for operation in the TV Bands, July 2011
U.S. FCC, ET Docket 08-260, “Second Report and Order and Memorandum Opinion and Order in the Matter of Unlicensed Operation in the TV Broadcast Bands,” November 14, 2008.
U.S. FCC, ET Docket 10-174, “Second Memorandum Opinion and Order in the Matter of Unlicensed Operation in the TV Broadcast Bands,” September 23, 2010.
NMEA 0183, Interface Standard of the National Marine Electronics Association, Version 4.00 http://www.nmea.org/content/nmea_standards/nmea_083_v_400.asp.
IETF RFC 2865, “Remote Authentication Dial In User Service (RADIUS),” June 2000.
[B1] DIAMETER/RFC 3588, “Diameter Base Protocol,” September 2003.
IETF RFC 3748, “Extensible Authentication Protocol (EAP),” June 2004.
Notes: doc.: IEEE 802.22-06/0006r0
January 2006
Gerald Chouinard, CRC
Page <number>