## Slide 1: Encoding of Data Structure (DS) in the Path Computation Element Communication Protocol (PCEP).
81st IETF @ Quebec
draft-dhody-pce-pcep-ds-00
Dhruv Dhody (dhruvd@huawei.com)
Udayasree Palle (udayasreepalle@huawei.com)

## Slide 2: Introduction
81st IETF @ Quebec
Backward-Recursive PCE-Based Computation (BRPC) defines VSPT [Virtual Shortest Path Tree] as a default de-facto data structure for PCRep message in inter-domain scenarios.
Need for multiple Data Structure based different scenarios like P2MP, Protection, HPCE, OF, Synchronization
PCEP is limited with just one Data Structure.
Extend PCEP to allow multiple data structures.

## Slide 3: Motivation for this work
81st IETF @ Quebec
[PCE-P2MP-PROCEDURES] describes the need for an extended VSPT for computation of the best core-tree.
[RFC 6007] describes the need for disjoint VSPT in case of Synchronized Dependent Path Computations.
VSPT does not fit into hierarchical PCE paradigm described in [PCE-HIERARCHY-FWK].
VSPT does not work well with constraints like HOP-LIMIT.
Since PCEP allow multiple Objective Function (OF); it is natural to extend PCEP to support multiple Data Structure based on path computation scenario

## Slide 4: PCEP Extension
81st IETF @ Quebec
DS-List TLV: Support advertisement of supported Data Structure (DS) in Open Message.
DS Object: In Request Message, it indicates the desired/required data structure to be applied by PCE. In Reply Message, it indicates the data structure that was used by the PCE during path computation and in the reply message.
New Flag in RP: Indicating PCE to supply DS in reply message.
Message Format: <DS> object is carried in PCReq / PCRep. It can be used in conjunction with SVEC as well as individual requests.

## Slide 5: Next Steps
81st IETF @ Quebec
Evaluate the need within the WG and extend PCEP accordingly.
IANA and security considerations needs analysis.

## Slide 6: Questions & Comments?
81st IETF @ Quebec

## Slide 7: Thanks!
81st IETF @ Quebec

## Slide 8: Backup Information
81st IETF @ Quebec
Inter Domain:
draft-zhao-pce-pcep-inter-domain-p2mp-procedures:

## Slide 9: Backup Information
81st IETF @ Quebec
Use of the Synchronization VECtor (SVEC) List for
Synchronized Dependent Path Computations:
RFC 6007

## Slide 10: Backup Information
81st IETF @ Quebec
PathList
PathList(i) =
For i=n: all possible paths meeting the constraints between BN-en(k,n) to destination
For 1<i<n: [all possible paths meeting the constraints between BN-en(k,i) to BN-ex(l,i)] + PathList(i+1)
For i=1: [all possible paths meeting the constraints between Source to BN-ex(l,1)] + PathList(2)