## Slide 1: Supporting explicit-path per destination in PCEP - P2MP Path Request.
81st IETF @ Quebec
draft-dhody-pce-pcep-p2mp-per-destination-00
Dhruv Dhody (dhruvd@huawei.com)
Udayasree Palle (udayasreepalle@huawei.com)
Note: Explicit Path here refers to the configured list of network elements that MUST be traversed or MUST be excluded in the final path computation.

## Slide 2: Introduction
81st IETF @ Quebec
PCEP is extended to support P2MP path computations in intra- & inter- domain scenarios.
Path Request message is defined as follows:
<IRO> is attached to all leaves and thus to only the common path.
Extend PCEP to define explicit-path per destination in P2MP context.

## Slide 3: Motivation for this work
81st IETF @ Quebec
In INTER-DOMAIN case different destinations will have different domain paths within the domain tree, it requires domain-sequence encoded in form of <IRO> to be attached per destination. It cannot be encoded for all destinations.
Administrator at the source can exert stronger control by providing explicit path (include, exclude, loose etc) per destination.
Compatibility: Basic MPLS TE P2MP Tunnel configurations for various operators support the configuration of explicit-path per destination.

## Slide 4: Example
81st IETF @ Quebec
Common Path
Common Path
Supporting configuration of <IRO> / <XRO> only for the common path is a disadvantage for the administrator in specifying network element and computation of final P2MP tree.
Explicit Path
Explicit Path cannot be applied!
Add 2 Destinations

## Slide 5: Path Request Message Format
81st IETF @ Quebec
Attach <IRO-List> / <XRO-List> to END-POINTS
<IRO> / <XRO> matches to destination in END_POINTS in ordered sequence

## Slide 6: Ordering Destinations in END-POINTS
81st IETF @ Quebec
The rule of the thumb is first <IRO> in <IRO-list> belongs to first destination in END-POINTS, the first <XRO> in <XRO-List> belongs to first destinations in END-POINTS etc..
Thus the order of the destinations in the END-POINTS is important.
Sometimes there may-be a need to split the destinations into multiple END-POINTS while encoding path-request message.

## Slide 7: Next Steps
81st IETF @ Quebec
Evaluate the need within the WG and extend PCEP accordingly.
IANA and security considerations needs analysis.

## Slide 8: Questions & Comments?
81st IETF @ Quebec

## Slide 9: Thanks!
81st IETF @ Quebec