## Slide 1: Generic Aggregation of Resource Reservation Protocol (RSVP) for IPv4 and IPv6 Reservation over PCN domains
Georgios Karagiannis, Anurag Bhargava
draft-karagiannis-pcn-tsvwg-rsvp-pcn-01
<number>
Notes: <number>

## Slide 2: Outline
Motivation
Main augmentations on Generic aggregated RSVP
Augmentations to PCN SM (Single Marking) and CL (Controlled Load) edge behavior drafts
Next steps
Examples of operation and new objects (not presented)
<number>
Notes: <number>

## Slide 3: Motivation (1)
PCN (Congestion and Pre-Congestion Notification) architecture (RFC 5559)
<number>
Notes: <number>

## Slide 4: Motivation (2)
All PCN charter items are fulfilled, except:
  Submit Encoding and Transport of PCN from Domain Egress to Ingress to the IESG for consideration as a Proposed Standard RFC
Pairs of PCN edge nodes use ingress-egress-aggregates (IEA):
  Need a signaling protocol to transport PCN information from PCN-egress-node to PCN-ingress-node and to maintain ingress-egress-aggregate between each pair of PCN edge nodes
<number>
Notes: <number>

## Slide 5: Motivation (3)
IETF QoS signaling protocols to solve problem:
Next Steps in Signaling Protocol (NSIS) subset (RFC 5971, RFC 5974, RFC 5979)
Aggregation of RSVP for IPv4 and IPv6 Reservations (RFC3175)
Generic Aggregate Resource ReSerVation Protocol (RSVP) Reservations (RFC4860)
All can be used, but for time being selected RFC 4860 due:
possible deployment interest
supports RFC 3175 and additional features such as:
  support of multiple IEAs from same pair of PCN edge nodes
  support of bandwidth reduction for individual flows (RFC 4495)
<number>
Notes: <number>

## Slide 6: Motivation (4)
<number>
Generic Aggregation of Resource Reservation Protocol (RSVP) for IPv4 and IPv6 Reservation over PCN domains architecture
Notes: <number>

## Slide 7: Main augmentations on Generic aggregated RSVP (1)
Four new (2 for CL and 2 for SM) objects specified to include PCN information to be transported from PCN-egress-node (Deaggregator) to PCN-ingress-node (Aggregator)
Support policies to initiate/maintain for each combination of PCN edge node and each of other PCN edge nodes one RSVP SESSION for generic aggregated reservations
  RSVP SESSION for generic aggregated reservations can match to one or more than one IEAs (between a pair of PCN edge nodes)
For each IEA, a PCN-egress-node, periodically generates Aggregated Resv messages and include new PCN object
PCN-interior-nodes are not using E2E RSVP or Generic Aggregated RSVP messages, but treat them as normal packets.
<number>
Notes: <number>

## Slide 8: Main augmentations on Generic aggregated RSVP (2)
E2E RSVP session admission in PCN-domain:
  each Aggregator support policies and PCN functionalities to admit or reject incoming e2e RSVP Path message & send a PathErr towards sender
E2E RSVP flow termination in PCN-domain:
  each Aggregator support policies and PCN functionalities for initiation:
    termination of one or more active E2E RSVP sessions
    reduce bandwidth of one or more active individual existing RSVP sessions, in order to solve congestion in PCN-domain
  same mechanisms for terminating or reducing bandwidth of an e2e RSVP session, as specified in [RFC4495]
<number>
Notes: <number>

## Slide 9: Augmentations to PCN SM and CL edge behavior drafts (1)
Considered that PCN-ingress-node collocated with Decision point
More than one IEAs between same pair of PCN edge nodes should be supported, each of them using a different PHB-ID value
When IEA supported by a PCN-ingress-node is in PCN-admission state, then based on local policy, requesting e2e RSVP session should be:
  rejected
  mapped to another IEA that NOT in PCN-admission-state
<number>
Notes: <number>

## Slide 10: Augmentations to PCN SM and CL edge behavior drafts (2)
When for IEA supported by PCN-ingress-node incoming traffic needs reduced then based on a local policy and for same IEA, selects a number of e2e RSVP sessions to be:
  terminated
  reduce reserved bandwidth of e2e RSVP sessions, in order to solve congestion in PCN-domain
<number>
Notes: <number>

## Slide 11: Next steps
We ask the support of the PCN WG or TSVWG such that this draft becomes either a PCN WG and/or a TSVWG working group draft
<number>
Notes: <number>

## Slide 12: Examples of operation and new objects
<number>
Notes: <number>

## Slide 13: Examples of operation and new objects
<number>
Notes: <number>

## Slide 14: Examples of operation and new objects
<number>
Notes: <number>

## Slide 15: Examples of operation and new objects
<number>
Notes: <number>