## Slide 1: Encoding 3 PCN-States in the IP header using a single DSCP draft-ietf-pcn-3-in-1-encoding-06.txt
Bob Briscoe, BT Toby Moncaster, independent Michael Menth, Uni Tuebingen
IETF-81 PCN Jul 2011
Notes: <number>

## Slide 2: status
<number>
Encoding 3 PCN-States in the IP header using a single DSCP
    mature draft: draft-ietf-pcn-3-in-1-encoding-06.txt
    dependency: RFC6040 (PS) not required but preferred
    intended status: standards track
    exec summary: rewritten to obsolete not just update RFC5696
      superset of SM in baseline, but threshold marker cannot set 11
      could not also accommodate PSDM
    immediate intent: Summarise ML discussions. Another WGLC
      06bis written to fix some nits, but can process with WGLC
 | DSCP | 00 | 10 | 01 | 11
Baseline RFC 5696 | DSCPn | Not-PCN | NM | EXP | PM
3-in-1 | DSCPn | Not-PCN | NM | ThM | ETM
Glossary
NM = Not Marked
ThM = Threshold Marked
ETM = Excess Traffic Marked
SM = single marking
PSDM = packet-specific dual marking
Notes: <number>

## Slide 3: 3-in-1 encoding rewritten
<number>
in order to obsolete, not just update, baseline [RFC5696]
  3-in-1 has become superset of 3-in-1 and single marking in baseline
  re-written not just pasted – clean text
clarified applicability
  particularly with respect to RFC6040 and pre-RFC6040 tunnels
added section on backward compatibility with baseline
imported relevant informative appendices from RFC5696 to 3-in-1
  Appendix A. Choice of Suitable DSCPs . . . . . . . . . . . . . . 17
  Appendix B. Co-existence of ECN and PCN . . . . . . . . . . . . 18
  Appendix C. Example Mapping between Encoding of PCN-Marks in
  IP and in MPLS Shim Headers . . . . . . . . . . . . . 21

## Slide 4: Summary of mailing list discussions
<number>
in order to obsolete, not just update, baseline encoding [RFC5696]
  3-in-1 has become superset of 3-in-1 and single marking in baseline
Cases where only one marking function throughout PCN domain
  Only Excess-traffic-marking: (e.g. single-marking) straightforward
  Only Threshold-marking: issues with pre-6040 tunnels (next slide)
Could not accommodate PSDM
  too many differences
  has to continue on experimental track as alternate to 3-in-1
tunnel half in a PCN-domain
  problem with RFC5559 text. Fix in 3-in-1? Or erratum to 5559?

## Slide 5: Threshold Marked (ThM) and pre-6040 tunnels
<number>
11 codepoint has become solely excess-traffic-marked (ETM)
  no longer generic ‘PCN-marked’ (PM, ie ETM or ThM) codepoint
  ThM now defined, but MUST NOT use unless all tunnel endpoints are RFC6040
  a pre-6040 tunnel egress conflicts with using ThM (reverts to NM on decap)
Summary of mailing list discussion that led to this decision…
We want to define cases where pre-6040 tunnel endpoints can be used
Easy cases:
  if only excess-traffic-marking throughout domain (e.g. single-marking - SM)
    just works with any tunnels
  if both marking functions running (e.g. controlled load - CL)
    all tunnel endpoints in PCN domain MUST comply with RFC6040
Harder case: if only threshold marking throughout domain (no example use-cases)
  We had two possibilities to choose between:
    threshold marking sets ThM but only in a pure 6040 PCN domain
    If pre-6040 tunnel endpoints present, allow ThM to set 11
  Given no use-case, decided not to allow case #2 (avoids confusion)
 | DSCP | 00 | 10 | 01 | 11
Baseline RFC 5696 | DSCPn | Not-PCN | NM | EXP | PM
3-in-1 | DSCPn | Not-PCN | NM | ThM | ETM

## Slide 6: tunnel half in a PCN-domain
<number>
in this case, PCN arch [RFC5559] incorrectly says
the tunnel egress node clears any PCN-marking on the inner header. This rule is applied before the "copy on decapsulation" rule above
incorrect: would break e2e ECN by wiping CE on inner
where to fix this
  3-in-1 appendix on interaction between e2e ECN and PCN
  Erratum to RFC5559?
tunnel ingress
tunnel egress
PCN ingress
PCN egress

## Slide 7: Encoding 3 PCN-States in the IP header using a single DSCP draft-ietf-pcn-3-in-1-encoding-06.txt
Q&A
Notes: <number>