## Slide 1: RFC 4601 Revision
81th IETF, Quebec
Rishabh Parekh
Jeffrey Zhang
Vero Zheng

## Slide 2: Motivation
Advance PIM specification to Draft Standard
  Address Errata
  Remove optional features that lack:
    Interoperable implementations
    Successful deployment experiences

## Slide 3: Presented in Prague Meeting
All errata had been reviewed
  No real technical issues
  Clarifications, editorial, keyword changes needed
Candidate feature-to-be-removed discussed and narrowed down to:
  (*, *, RP)
  Group-to-RP mapping
Milestones
  Draft -00 end of April, addresses errata
  Draft -0x before Quebec meeting, removes certain features

## Slide 4: Current Status
Errata addressed in draft-parekh-pim-rfc4601bis-00
Features removed in -01:
  (*, *, RP)
    Positive response and no objection on mailing list
  PMBR related sections and appendices
    (*, *, RP) is the foundation for PMBR
Group-to-RP mapping kept:
  Was going to remove, and refer to RFC 6226
  That would cause a down-ref problem
    Draft Standard referring to a Proposed Standard

## Slide 5: No more PMBR functionality?
Somewhat drastic even to us
  No more mentioning of border router at all
Is really justified after some pondering:
  No major vendors implemented (*,*,RP), which is the foundation of PMBR as described in RFC 4601 and RFC 2715
    Only documented (RFC 4602) implementation is XORP (open source)
      Deployment experience?
  MSDP is typically used for inter-sparse-domain
  Some proprietary mechanisms for downstream dense domains
    Instead of relying on (*,*,RP) & PMBR

## Slide 6: Other minor changes in -01
Some keywords
Removed a redundant “CouldAssert” condition in (S,G) assert state machine
  In case of “receiving inferior assert at NI”
“Cancels the (S,G) Assert Timer” -> “Expires …”
  Summary of Assert Rules and Rationale, #6
Do not attempt to aid SSM-unaware legacy routers
  Section 4.8.1, SSM rules
Appendix B (Index) removed

## Slide 7: Next Steps
WG adoption?
Survey, review & feedback, especially on features to be removed:
  (*,*,RP) & PMBR ok?
  Any others?