## Slide 1: PIM ECMP Assert
draft-hou-pim-ecmp-01
IETF 81, Quebec City
Notes: <number>

## Slide 2: Existing ECMP RPF Overview
There are two ways to choose an RPF path when ECMP is present
  Select the path whose gateway is the PIM neighbour with the largest IP address
  Use a hash algorithm
ECMP RPF selection is downstream driven
  Limited by routing/hash algorithm, no other factors considered
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 3: Existing ECMP RPF Issues
Load-balancing is based on IP addresses instead of “loads”
Same flow might be sent onto two links
  Waste of bandwidth
  Especially if an implementation chooses to stick to its RPF selection after link/node failure
“Assert” only chooses an RPF neighbour within a LAN, but not between ECMP paths
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 4: PIM ECMP Assert
PIM ECMP Assert is proposed to improve control of RPF path selection.
  Initiated by upstream routers (similar to Assert)
  Used to choose a path
    based on administrative choice
    from ECMP path
  Allow downstream routers to use information such as available bandwidth to choose an RPF neighbour
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 5: PIM ECMP Assert
Design Consideration
  Minimize control traffic in steady state
  Minimize unnecessary traffic disruption
  Allow for future enhancement to include more criteria for choosing a path
We are OPEN to a different name
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 6: PIM ECMP Assert
Key features
  Triggered by PIM Joins
  Sent in a different subnet (used to choose a path, instead of an RPF neighbour)
  New PIM Hello Options
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 7: Comparing to PIM Assert
Trigger
  Assert is data driven
  ECMP Assert is triggered by Join
Application
  Using Assert to choose an RPF neighbor within a subnet
  Using ECMP Assert to choose a path from ECMP
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 8: Comparing to PIM Assert
Impact
  Assert modifies “routing” decision by comparing routing metrics sent by upstream routers
  ECMP Assert preserves routing decision (ECMP)
  ECMP Assert compares non-routing metric (such as uptime/timestamp, bandwidth etc…)
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 9: Example (PIM Assert)
IETF 81
draft-hou-pim-ecmp-01
<number>
A
B
C
D
sources
receivers
RPF is Red/A
RPF is Red/B
Assert
Assert
Notes: <number>

## Slide 10: Example (PIM ECMP Assert)
IETF 81
draft-hou-pim-ecmp-01
<number>
A
B
C
D
sources
receivers
RPF is Red/A
Assert Red/A in Blue
Assert Blue/B in Red
RPF is Blue/B
Notes: <number>

## Slide 11: Packet Format: ECMP Assert
0 1 2 3
A0A1A2A3A4A5A6A7A8A9B0B1B2B3B4B5B6B7B8B9C0C1C2C3C4C5C6C7C8C9D0D1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PIM Ver | Type | Reserved | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address (Encoded-Group format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address (Encoded-Unicast format) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Neighbor Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+-+-+-+-+-+- +-+-+-+-+-+-+-+-+............ Interface ID ........... -+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Preference | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-- ............. Metric …......... -+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+-+-+- ….. Metric ….. +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+-+-+-+-+-+-+-+-+-+-+-+
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 12: Packet Format: Hello Option
PIM Hello Options
IETF 81
draft-hou-pim-ecmp-01
<number>
ECMP Assert Hello Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = TBD | Length = 0 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: <number>

## Slide 13: Update From -00
Added new authors
Clarified operation on transient cases
Clarified use of PIM Interface-ID
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>

## Slide 14: For The Working Group
The draft addresses a weakness in PIM RPF selection
There is practical application that requires a solution like this
We welcome comments/suggestion from the working group
We’d like to request the working group to adopt this I-D
IETF 81
draft-hou-pim-ecmp-01
<number>
Notes: <number>