## Slide 1: PPSP NAT traversal
Lichun Li, Jun Wang, Wei Chen
{li.lichun1, wang.jun17}@zte.com.cn
chenweiyj@chinamobile.com
draft-li-ppsp-nat-traversal-02
Notes: <number>

## Slide 2: Changes since 01
Make change to PPSP-ICE solution
  Peer tries to contact remote peer’s host addr and reflexive addr first.
  If it fails, it turns to exchange ICE parameters and perform ICE process.
Propose PPSP protocol extensions for NAT traversal
  Mainly based on gu-ppsp-tracker-protocol and gu-peer-protocol
  Mainly required by PPSP-ICE.
  RELOAD-ICE may also use some extensions.
<number>
Notes: <number>

## Slide 3: NAT traversal solution overview
  ICE is the standard NAT traversal solution.
  ICE requires application to exchange ICE parameters.
  Two solutions in the draft: PPSP-ICE and RELOAD-ICE
    both use ICE
    but use PPSP and RELOAD separately to exchange ICE parameters (candidates and credentials for connectivity check).
  Candidate
    Candidate (from ICE RFC5245): A transport address that is a potential point of contact for receipt of media.
    Assigned by host itself, NAT device or relay node.
    NATed peers need NAT devices or NAT traversal service nodes to discover/assign candidates.
<number>
Notes: <number>

## Slide 4: NAT traversal service nodes and candidates
Dedicated STUN/TURN server
  TURN: application-agnostic relay, assign relayed candidates to NATed peers
  STUN: Discover reflexive candidates for NATed peers
STUN/TURN peer
  Peer providing STUN/TURN service
Proxy peer (mandatory for PPSP-ICE)
  Peer providing application layer relay. Analogy to SIP or RELOAD relay
  Assign proxy candidates to NATed peers
STUN-like tracker
  Tracker providing STUN-like function with PPSP message. E.g. tracker informs peer its reflexive candidate in PPSP CONNECT response.
  Compared with STUN server/peer, STUN-like tracker saves messages.
  Analogy to SIP rport
<number>
Notes: <number>

## Slide 5: PPSP-ICE: Discover STUN/TURN/proxy peer via tracker
STUN/TURN/proxy peer report their abilities to tracker
NATed peer fetches STUN/TURN/proxy peer list from tracker
NATed peer obtains candidates from STUN/TURN/proxy peer
<number>
Notes: <number>

## Slide 6: PPSP-ICE solution (signal traversal)
candidates
  Host addr, reflexive addr
  Relay required: relayed addr, proxy addr
Strategy to connect
  contact host addr and reflexive addr directly first
  contact proxy addr to exchange ICE parameters
Exchange ICE parameters with PPSP messages called Attach
<number>
Notes: <number>

## Slide 7: PPSP-ICE solution (media traversal)
After PPSP connection is built, media connection can be built.
To build media connection, ICE parameters are exchanged using PPSP messages called MediaAttach
<number>
Notes: <number>

## Slide 8: Attach & MediaAttach
<DestPeerID>***</DestPeerID>
<PeerID>***</PeerID>
<SDP> ... </SDP>
SDP contains ICE parameters.
Mandatory for PPSP-ICE solution
Also required if there is no NAT
Notes: <number>

## Slide 9: Tracker's STUN-like Function
Optional for both PPSP-ICE and RELOAD-ICE solutions.
Peer discovers its reflexive addr with tracker’s help.
Put <ReflexiveAddr> IP and port </ReflexiveAddr> in CONNECT response.

## Slide 10: Proxy peer
Mandatory for PPSP-ICE solution
NATed peer reuses CONNECT to establish connection with proxy peer, and obtain proxy cadidate
Notes: <number>

## Slide 11: STUN/TURN/proxy Ability Report
Mandatory for PPSP-ICE solution, optional for RELOAD-ICE solution
gu-ppsp-tracker-protocol already supports STUN/TURN ability report with STAT method
Add a STAT type “proxy” to support proxy ability report
Notes: <number>

## Slide 12: Find STUN/TURN/proxy Peer List
Mandatory for PPSP-ICE solution, optional for RELOAD-ICE solution
Fetch STUN/TURN/proxy peer list from tracker with modified FIND method
Remove <SwarmID> and <ChunkID> from FIND request
<PeerID>***</PeerID>
<Peernum>***</Peernum>
<Stats>
<Stat property="STUN">true</Stat>
... more stats ...
</Stats>
Notes: <number>

## Slide 13: Report Candidates to Tracker
Peer puts <PeerAddresses> in JOIN/JOIN_CHUNK request
<PeerAddresses>
<PeerAddress ip="***" port="***" priority="***" type="host"/>
<PeerAddress ip="***" port="***" priority="***" type="reflexive"/>
<PeerAddress ip="***" port="***" priority="***" type="proxy"/>
</PeerAddresses>
Mandatory for PPSP-ICE solution
Also required to support multi-homed peer
Notes: <number>

## Slide 14: About NAT traversal extension
Leave the choice of NAT traversal to implementation
  In some scenarios, NAT traversal is not necessary.
    no NAT
    QoE is satisfied without NAT traversal.
  There are multiple NAT traversal solution/methods requiring different protocol extension.
Base protocol is mandatory to implement, while NAT traversal extension is not?
  Base protocol should work without NAT traversal, and allow NAT traversal extension

## Slide 15: Next Step
Get more comments
Call on participation in the draft
Refine NAT-traversal extensions
<number>
Notes: <number>

## Slide 16
<number>
Notes: Thank you!
<number>

## Slide 17
<number>
Notes: Thank you!
<number>

## Slide 18
<number>
Notes: Thank you!
<number>

## Slide 19: NAT traversal necessity
Scenarios need NAT traversal: The ratio of NATed peer is high in the swarm. Without NAT traversal, some peers can't download or take long time to download needed chunks.
Scenarios don't need NAT traversal: There is no NAT or the QoE is satisfied without NAT traversal solution.
NAT traversal is necessary at least in some P2P streaming systems (e.g. UUSee).
<number>
Notes: The necessity of NAT traversal depends on scenarios.
#Some Scenarios need NAT traversal.
In some Scenarios, the ratio of NATed peer is high in the swarm. Without NAT traversal, some peers can't download or take long time to download needed chunks.
In some other scenarios, there is no NAT or the QoE is satisfied without NAT traversal solution.
Any way, NAT traversal is necessary at least in some P2P streaming systems (e.g. UUSee).
<number>

## Slide 20: Implementation consideration
The decision of supporting NAT traversal or not should be left to implementation.
The choices of NAT traversal solution/method, NAT traversal service node and NAT traversal service discovery method should be left to implementation too.
Implementation considerations: the ratio of NATed peer, the ratio of each NAT type, implementation overhead, etc.
<number>
Notes: The decision of supporting NAT traversal or not should be left to implementation.
The choices of NAT traversal solution/method, NAT traversal service node and NAT traversal service discovery method should be left to implementation too.
To make these choices, Implementation should consider things like the ratio of NATed peer, the ratio of each NAT type, implementation overhead and so on.
<number>