## Slide 1: draft-cohn-mpls-tp-pw-protection-01
IETF 81 Jul 2011
Daniel Cohn (danielc@orckit.com)
Rafi Ram (rafir@orckit.com)
Ma Yuxia (ma.yuxia@zte.com.cn)
Masahiro Daikoku (ms-daikoku@kddi.com)

## Slide 2: Problem Statement (1)
MPLS-TP transport path recovery requirements (RFC 5654, section 2.5) apply to PW as well as to LSP
  "In an MPLS-TP environment, a transport path corresponds to an LSP or a PW”
MPLS-TP Survivability Framework (draft-ietf-mpls-tp-survive-fwk-06) specifies that the “functional architecture…applies to both LSP and PWs”
However, MPLS WG linear protection draft (draft-ietf-mpls-tp-linear-protection-07) does not explicitly describe mechanisms for PW protection in MPLS-TP

## Slide 3: Problem Statement (2)
PW linear protection is required to protect MS-PW in the event of S-PE node failure
  Protection against link failure events can be more efficiently provided by LSP linear protection (working and protection LSP shown in blue and red respectively)

## Slide 4: Proposed Solution
The draft is an applicability statement that applies the LSP linear protection mechanism in draft-ietf-mpls-tp-linear-protection-07 to MPLS-TP MS-PW
Specifically:
  References to OAM indications apply as referring to MS-PW OAM, provided by PMEG
  References to LER apply as referring to T-PE
  References to server layer apply to the LSPs over which MS-PW is carried
  PSC protocol PDUs are encapsulated in PW associated channel (RFC 4385)

## Slide 5: Benefits (1)
Compliance with MPLS-TP PW protection requirements with full reuse of LSP linear protection concepts and mechanism from draft-ietf-mpls-tp-linear-protection-07
  With consequent reuse of existing LSP linear protection implementation

## Slide 6: Benefits (2)
Unlike other PW redundancy proposals (e.g. draft-ietf-pwe3-redundancy-bit-04), this draft meets MPLS-TP requirements (RFC 5654, draft-ietf-mpls-tp-survive-fwk), such as:
  Support for 1:1 and 1+1 schemes
  Handling of coexisting triggers
  Ability to distinguish administrative recovery actions from other triggers
  Full support of revertive/nonrevertive
  Full support of administrative triggers
  Requirement of fast retransmission of PSC messages (faster recovery in message loss scenario)
  1-phase protocol (faster recovery)
  Support of hold-off timer (to avoid race conditions)

## Slide 7: Next Steps
Incorporate input into next draft
Request working group adoption

## Slide 8: Thank You
Questions ? Comments ?