## Slide 1: Pseudowire Endpoint Fast Failure Protection draft-shen-pwe3-endpoint-fast-protection-00
Rahul Aggarwal (rahul@juniper.net)
Yimin Shen (yshen@juniper.net)
IETF 81, Quebec City, Canada

## Slide 2: Overview
PW egress endpoint failures:
  AC
  PE
Global repair mechanisms rely on multi-homed CE and PW redundancy. Control plane convergence may be relatively slow.
This draft proposes local repair to complement global repair.
  Protection against both egress AC and PE failures.
  Fast restoration in the order of 10s of milliseconds, comparable to FRR.
  LDP and BGP signaled PWs.
CE1
CE2
PE1
PE2 (primary)
PE3
PE4 (backup)
PW1 (primary)
PW2 (backup)
PE failure
AC failure
global repair

## Slide 3: Overview (cont.)
CE1
CE2
PE1
PE2 (primary)
PLR
PW1 (primary)
PW2 (backup)
AC failure
PE4 (backup)
protector
PE3
CE1
CE2
PE1
PE2 (primary)
PE3
PE4 (backup)
protector
PW1 (primary)
PW2 (backup)
PE failure
PLR

## Slide 4: Terminology
Segment: The set of ACs that a multi-homed CE uses to connect to PEs for a given emulated service.
Context ID: A unique IP-v4 address that is assigned to a segment. It is advertised by both primary PE and the protector PE in IGP as a stub link.
PLR (point of local repair): The router where a failure is detected and local repair is performed.
  AC failure: primary PE.
  PE failure: peultimate hop of PW transport LSP.
Protector PE: A PE that protects a segment, and receives PW packets from PLR upon a failure.
Bypass LSP: An LSP used by PLR to tunnel PW packets to a protector PE upon a failure.
  Destination is context ID.
  UHP (ultimate hop popping).
CE1
CE2
PE1
PE2 (primary)
PW1 (primary)
PW2 (backup)
segment (context ID)
PE3
PE4 (backup)
protector
primary AC
backup AC

## Slide 5: Procedure for AC Failure
PE2 (PLR) sets up local protection.
  A bypass LSP is established to PE4 (protector PE).
    Destination = context ID.
    Requires UHP.
  Upon a failure, PE2 tunnels PW packets to PE4 via bypass LSP.
    PW label remains unchanged.
CE1
CE2
PE1
PE2 (primary)
PLR
PW1 (primary)
PW2 (backup)
AC failure
PE4 (backup)
protector
PE3
bypass LSP

## Slide 6: Procedure for AC Failure (cont.)
PE4 (protector PE) sends packets to CE2 based on PW label (i.e. upstream label) assigned by PE2.
  Learns {PWid, label, context ID} from PE2 via LDP.
    PWid: newly defined Protection FEC Element.
    Label: Upstream Assigned Label TLV.
    Context ID: Logical Interface ID in IF_ID TLV.
  Installs forwarding state for PW label in a context-specific label space indicated by context ID.
  Allocates a non-reserved label for bypass LSP, pointing to this label space.
  Performs 2 label lookups during forwarding:
    1st lookup based on bypass LSP’s label finds context-specific label space.
    2nd lookup based on PW label in context-specific label space results in sending packet to CE2.
CE1
CE2
PE1
PE2 (primary)
PLR
PW1 (primary)
PW2 (backup)
AC failure
PE4 (backup)
protector
PE3
bypass LSP

## Slide 7: Procedure for PE Failure
PLR is the penultimate hop of PW transport LSP.
If RSVP is the signaling protocol, PLR should
  Signal bypass LSP based on “node protection desired” flag in Path message of transport LSP.
  Report node protection available and in-use status in RRO of Resv message.
  Node protection FRR for LSP egress.
CE1
CE2
PE1
PE2 (primary)
PE3
PE4 (backup)
protector
PW1 (primary)
PW2 (backup)
PE failure
PLR
bypass LSP

## Slide 8: Protection Models
Co-located protector PE
  Protector PE is a backup PE, co-located with primary PE on a segment.
  Has a direct connection to CE via a backup AC.
  PW label popping.
  Context ID allocation may typically be per {primary PE, protector PE}.

## Slide 9: Protection Models (cont.)
Centralized protector PE
  One PE protects all segments for all primary PEs.
  May not be a backup PE on all segments.
  For a segment with no direct connection, it must:
    Learn {Protection FEC, label, context ID} from a backup PE via LDP.
    Swap primary PE’s PW label to backup PE’s PW label, and send packet to backup PE.
  Only one context ID is needed per primary PE.
CE1
CE2
PE1
PE2 (primary)
PE3
PE4 (backup)
PW1 (primary)
PW2 (backup)
PE failure
PLR
bypass LSP
PE5
protector

## Slide 10: Next Steps
Questions and comments?
WG adoption?