## Slide 1: LDP Extensions for MPLS-TP PW Proactive OAM Configuration draft-zhang-mpls-tp-pw-oam-config-05
PWE3/MPLS WG, IETF 81th, Quebec
Fei Zhang Bo Wu
Elisa Bellagamba Attila takacs
Xuehui Dai Min Xiao

## Slide 2: Update
Add two bits “C” “V” in the MPLS-TP PW OAM Capability TLV
The MPLS-TP PW OAM capability negotiation is done by the Initialization message exchanges
  There are only two bits unused in the CV field of the VCCV parameter ID
“C": CC supported [CC-CV-RDI]
“V”: CV supported [CC-CV-RDI]
[RFC5085]
[RFC5885]

## Slide 3: Backward compatibility
If both the two T-PEs can support the CC or CV function defined in [CC-CV-RDI], the BFD configuration procedure is adopted.
  The C or V flag of MPLS-TP PW OAM Capability TLV MUST be set
  The C or V flag of MPLS-TP PW OAM Configuration TLV MAY be set
  The BFD Configuration sub-TLV MAY be carried
The revised MPLS-TP PW OAM Configuration TLV
  More compact [draft-ietf-mpls-lsp-ping-mpls-tp-oam-conf]
If at least one of the two T-PEs do not support the CC or CV operation, [RFC5885] will be performed.
  The C and V flags of MPLS-TP PW OAM Configuration TLV MUST NOT be set
  The BFD Configuration sub-TLV MUST NOT be carried
The described behavior ensures full compatibility with the existing implementations.
  Thanks Greg、Matthew、Luca for the discussion

## Slide 4: Next Steps
Comments/Feedback?
Keep in parallel with the related work done in MPLS-TP
  draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
  draft-ietf-mpls-lsp-ping-mpls-tp-oam-conf
Adopted as a WG document?