## Slide 1: Pseudowire Communities draft-pkwok-pwe3-pw-communities-01
Paul Kwok
Pranjal Dutta
Frederic Jounay
draft-pkwok-pwe3-pw-communities-01
IETF-81

## Slide 2: Objectives
Generic method to simplify provisioning dynamic Pseudowires.
Aid in policy administration during dynamic multi-segment pseudowire (Dyn MS-PW) set-up across various S-PEs with minimal overhead.
IETF-81
draft-pkwok-pwe3-pw-communities-01

## Slide 3: Problem Statement
Dyn MS-PW spans across multiple administrative domains. For security reasons strict access control is required at S-PEs. One way is to define policies at S-PEs based on SAII/TAII but adds complexity, administrative overheads, configuration mistakes.
Dyn MS-PW requires each S-PE to choose a unidirectional PSN tunnel to bind to a PW. T-PEs may require to signal the preference of PSN tunnels at S-PEs. Signaling each of the various types of PSN tunnel selection criteria adds significant burden to LDP messaging procedures.
IETF-81
draft-pkwok-pwe3-pw-communities-01

## Slide 4: Solution
A “PW community” attribute as a 32 bit identifier carried in an Interface Parameters Sub-TLV.
A PW community represents a template that has set of rules defined locally by a T-PE or S-PE.
Each T-PE or S-PE can define its own set of rules and it is upto the administrative domain(s) to maintain congruities among PW community rules.
IETF-81
draft-pkwok-pwe3-pw-communities-01

## Slide 5: Solution contd..
Very generic method and any complex rules can be mapped to specific PW communities.
Can be considered as “Coloring” of PWs so that PW set-up decisions can be based on identity of the group.
Concept is different from PW Grouping ID . It is not necessary that PW Grouping and PW communities be correlated.
IETF-81
draft-pkwok-pwe3-pw-communities-01

## Slide 6: Next Steps
Request discussions/feedbacks in mailing list.
WG Status?
IETF-81
draft-pkwok-pwe3-pw-communities-01