## Slide 1: LDP extensions for Explicit Pseudowire to transport LSP mapping
draft-cao-pwe3-mpls-tp-pw-over-bidir-lsp-03.txt
Mach Chen (mach.chen@huawei.com)
Wei Cao (wayne.caowei@huawei.com)
Attila Takacs (Attila.Takacs@ericsson.com)
Ping Pan (ppan@infinera.com)
IETF 81th PWE3 WG Quebec City

## Slide 2: Problem Statement
IETF 81th PWE3 WG Quebec City
AC’s
PE2
PE1
PW’s
P2
P1
PW’s
AC’s
AC’s
AC’s
Bidirectional LSP
Today,
  A bi-directional connection creates two PW’s, which may use two independent LSPs as PSN Tunnels
  The PE’s select and bind PW’s to PSN Tunnel, with no control plane support
Here is the new service requirements:
  mapping bi-directional circuits to bi-directional LSP’s (or co-routed LSP’s)
Need to have explicit control over PW-LSP binding at control-plane

## Slide 3: Solution Overview (Single-Hop) (Strict Mode)
IETF 81th PWE3 WG Quebec City
AC’s
PE2
PE1
P2
P1
AC’s
AC’s
AC’s
PSN 1
PSN 2
Setup PW1 using PSN1;
Make sure PW2 using PSN 1
PW1
PW2
OK
Notes: <number>

## Slide 4: Solution Overview (Single-Hop) (Congruent Mode)
IETF 81th PWE3 WG Quebec City
AC’s
PE2
PE1
P2
P1
AC’s
AC’s
AC’s
PSN 1
PSN 2
Setup PW1 using PSN1;
Make sure PW2 is on the same PSN
PW1
PW2
OK
or, NO!
A PW has been initiated, or,
It does not want to use PSN1
Notes: <number>

## Slide 5: Solution Overview: Tunnel Representation
AC
AC
PE2
PE1
P2
P1
IETF 81th PWE3 WG Quebec City
P4
P3
Working LSP
Protecting LSP with Make Before Break
For Make-before-break LSP’s, the Tunnel-ID’s are the same
No need to signal LSP-id, if a PSN has protection
  Also, this avoids LDP PW re-signaling overhead
The protocol needs to have the option to signal Tunnel-ID only
Notes: <number>

## Slide 6: Solution Overview (Multi-Segment) (Strict Mode)
IETF 81th PWE3 WG Quebec City
AC’s
PE3
PE1
PE2
AC’s
AC’s
AC’s
PSN 1
PSN 2
(1)
Setup PW1 using PSN1;
PW2 needs to be PSN 1
PW1
PW2
PSN 3
PSN 4
PW4
PW3
(2)
Setup PW3 using PSN3;
PW4 needs to be PSN 3
(3) OK
(4) OK
Notes: <number>

## Slide 7: Protocol Extension
Made significant changes based on the feedback from last IETF and mailing list
PSN Tunnel Binding TLV
IPv4 PSN Tunnel sub-TLV format

## Slide 8: Protocol in Summary
Support two types of PW’s
  SS-PW: both PEs could be Active or Passive
  MS-PW (FEC 129 only): always active from the headend
Binding Types:
  Strict binding (S-bit MUST be set)
  Congruent binding( C-bit MUST be set)
  C-bit and S-bit MUST be mutually exclusive from each other
IETF 81th PWE3 WG Quebec City

## Slide 9: Next steps
Comments?
WG document?
IETF 81th PWE3 WG Quebec City